## Slide 1: Day 18
Kalman Filter

## Slide 2: Plant or Process Model
describes how the system state changes as a function of time, control input, and noise
  state at time k
  control inputs at time k
  process noise at time k
  state transition model or matrix
  control-input model or matrix

## Slide 3: Measurement Model
describes how sensor measurements vary as a function of the system state
  sensor measurement at time k
  sensor noise at time k
  observation model or matrix

## Slide 4: Kalman Filter
the Kalman filter is a provably optimal (in terms of least-squared error) algorithm for fusing sensor measurements to produce an estimate of the state and the state covariance
  state at time k
  state covariance at time k

## Slide 5: Kalman Filter
the Kalman filter estimates a process in two stages
  prediction: current state and state covariance estimates are projected forward in time to predict the new state and state covariance
    “time update equations”
  correction: the sensor measurements are incorporated into the predicted state to obtain improved estimates of the state and state covariance
    “measurement update equations”
time update
(predict)
measurement update
(correct)

## Slide 6: Kalman Filter Algorithm
Initialization
  choose (guess) initial values for state and state covariance estimates

## Slide 7: Kalman Filter Algorithm
Prediction:
  predict the next state using the plant model
  state covariance grows (because we are not incorporating the sensor measurements yet)
    covariance of the plant noise

## Slide 8: Kalman Filter Algorithm
Correction: correct the predicted state using the sensor measurement
  expected value of measurements (from measurement model)
  difference between actual and expected measurements
  measurement covariance
  Kalman gain

## Slide 9: Kalman Filter Algorithm
State and state covariance:
  new state estimate incorporating most recent measurement
  new state covariance estimate