## Slide 1: Potential Functions
in continuous space potential functions can be used for path planning
a potential function is a differentiable real-valued function U
  i.e., U assigns a scalar real value to every point in space
potential functions you might know
  gravitational potential
  electrostatic potential

## Slide 2: Goal Potential
the goal potential should be an attractive potential
  small near the goal
  large far from the goal
  monotonically increasing
    nice too if it is continuously differentiable

## Slide 3: Goal Potential
consider the quadratic potential
goal
located at a minimum in U
“rolls” towards the goal

## Slide 4: Goal Potential
“rolling towards the goal” can be accomplished using gradient descent
gradient descent
  starting at initial configuration, take a small step in the direction opposite to the gradient F until |F| = 0

## Slide 5: Goal Potential
notice that the wave-front planner basically works this way
  it defines a potential where there is only one minimum
    the minimum is located at the goal
  it then uses gradient descent to move towards the goal
17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2
18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3
19 | 18 | 1 | 1 | 15 | 14 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
20 | 19 | 1 | 1 | 16 | 15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
21 | 20 | 1 | 1 | 17 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 1 | 1 | 37 | 38
1 | 1 | 1 | 1 | 18 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 1 | 1 | 36 | 37
1 | 1 | 1 | 1 | 19 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 1 | 1 | 35 | 36
0 | 0 | 1 | 1 | 20 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 1 | 1 | 34 | 35
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 23 | 24 | 1 | 1 | 1 | 1 | 33 | 34
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 24 | 25 | 1 | 1 | 1 | 1 | 32 | 33
0 | 0 | 1 | 1 | 29 | 28 | 27 | 26 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
0 | 0 | 1 | 1 | 30 | 29 | 28 | 27 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33
0 | 51 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 33 | 34
51 | 50 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 34 | 35
50 | 49 | 48 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 36
51 | 50 | 49 | 47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 37
start

## Slide 6: Day 26
Potential Functions (cont)

## Slide 7: Obstacle Potential
obstacles should have a repulsive potential to keep the robot away from the obstacle
  the repulsive force should increase closer to the obstacle
  often modeled as a potential barrier that rises to infinity as the robot approaches the obstacle; for example
  where qobstacle is the closest point on the obstacle

## Slide 8: Obstacle Potential
to infinity
approaches
U=0
approaches
U=0

## Slide 9: Obstacle Gradient
gradient +’ve
gradient -’ve

## Slide 10: Obstacle Potential
one problem with the previous obstacle potential
  potential (and gradient) is always non-zero away from the obstacle
    an obstacle far away from the robot will influence the path

## Slide 11: Obstacle Potential
possible solution
  choose a potential function that equals zero a distance Q* away from the obstacle
  where D(q) is the distance between the robot and the obstacle

## Slide 12: Obstacle Potential
to infinity
U=0
U=0

## Slide 13: Obstacle Gradient
gradient +’ve
gradient -’ve
| gradient | = 0
| gradient | = 0

## Slide 14: Total Potential
the total potential field is simply the sum of the attractive and repulsive potentials
  where q is the location of the robot

## Slide 15: Multiple Obstacles
one approach for multiple obstacles is to consider only the nearest obstacle
  this can lead to oscillating paths when the robot is almost equidistant to two or more obstacles

## Slide 16: Multiple Obstacles
attractive force (goal)
repulsive force (obstacle)
nearest obstacle point

## Slide 17: Multiple Obstacles

## Slide 18: Multiple Obstacles

## Slide 19: Multiple Obstacles

## Slide 20: Multiple Obstacles

## Slide 21: Multiple Obstacles

## Slide 22: Multiple Obstacles
an alternative approach is to consider the contributions to the total potential from all obstacles
  where Uobstacle, i is the repulsive potential contribution from the ith obstacle

## Slide 23: Computing Distances on a Grid
the brushfire algorithm can be used to compute distances on a grid where
  free space is labeled with a 0
  obstacles are labeled with a 1
outputs
  grid labels equal to the distance to the nearest obstacle
    grid labels can be used to compute gradients
like the wave-front planner, you need to decide between 4- and 8-connectivity

## Slide 24: Brushfire Algorithm
for each cell labeled 1
label each adjacent free-space cell with 2
L := 2
do
for each cell labeled L
label each adjacent free-space cell with L+1
L := L+1
while there are still free-space cells remaining

## Slide 25: Brushfire Algorithm
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 26: Brushfire Algorithm
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 2 | 2 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 0 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 0 | 2 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 2 | 1 | 2 | 0 | 2 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 0 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 27: Brushfire Algorithm
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 3 | 0 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 0 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 3 | 3 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 3 | 2 | 3 | 0 | 3 | 2 | 3 | 0 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 2 | 1 | 2 | 3 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 1 | 2 | 3 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 0 | 0 | 0 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 28: Brushfire Algorithm
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 4 | 0 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 4 | 0 | 0 | 4 | 3 | 2 | 1
1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 0 | 0 | 0 | 4 | 3 | 2 | 1
1 | 2 | 3 | 4 | 4 | 4 | 4 | 4 | 0 | 0 | 0 | 0 | 4 | 3 | 2 | 1
1 | 2 | 3 | 3 | 4 | 0 | 4 | 3 | 4 | 0 | 0 | 0 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 3 | 4 | 3 | 2 | 3 | 4 | 0 | 0 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 2 | 1 | 2 | 3 | 4 | 0 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 1 | 2 | 3 | 4 | 0 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 4 | 4 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 29: Brushfire Algorithm
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 4 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 4 | 5 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 5 | 0 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 4 | 4 | 4 | 4 | 4 | 5 | 0 | 0 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 3 | 4 | 5 | 4 | 3 | 4 | 5 | 0 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 3 | 4 | 3 | 2 | 3 | 4 | 5 | 5 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 2 | 1 | 2 | 3 | 4 | 5 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 1 | 2 | 3 | 4 | 5 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 4 | 4 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 30: Brushfire Algorithm
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 3 | 4 | 4 | 4 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 4 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 4 | 5 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 5 | 6 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 4 | 4 | 4 | 4 | 4 | 5 | 6 | 6 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 3 | 4 | 5 | 4 | 3 | 4 | 5 | 6 | 5 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 3 | 4 | 3 | 2 | 3 | 4 | 5 | 5 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 3 | 2 | 1 | 2 | 3 | 4 | 5 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 2 | 2 | 2 | 1 | 2 | 3 | 4 | 5 | 4 | 3 | 2 | 1
1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 4 | 4 | 4 | 3 | 2 | 1
1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 1
1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 31: Brushfire Algorithm
the gradient of distance at a cell is determined by computing differences with neighboring cells