## Slide 1: Day 27
Visibility Graphs

## Slide 2: Introduction
if we have to frequently plan paths on a static environment then it makes sense to use a data structure that supports efficient planning of subsequent paths
  e.g., visibility graph
    nodes correspond to vertices of polygonal obstacles
    edges correspond to paths between nodes

## Slide 3: Roadmaps
consider the highways (in orange) in the GTA

## Slide 4: Roadmap
definition:
  A union of one-dimensional curves is a roadmap (RM) if for all starting points (qstart) and goal points (qgoal) in freespace (Qfree) that can be connected by a path the following properties hold:
  Accessibility
    there exists a path from qstart to some q'start  RM
      i.e., the robot can reach the roadmap from the start point
  Departability
    there exists a path from q'goal  RM to qgoal
      i.e., the robot can depart the roadmap to reach the goal point
  Connectivity
    there exists a path in RM from q'start to q'goal
      i.e., there is a path on the roadmap connecting the start and depart points

## Slide 5: Visibility Graph
defined for 2D space with polygonal obstacles
a graph where
  nodes
    {qstart, qgoal, and vertices of all obstacles }
  edges
    connect all pairs of nodes ni and nj that are visible to one another

## Slide 6: Visibility Graph
contains the shortest path between the start and goal
* normally the start and goal points are included in the graph

## Slide 7: Visibility Graph Construction
start by drawing lines of sight from start and goal to all visible vertices

## Slide 8: Visibility Graph Construction
next, draw lines of sight from every vertex of every obstacle
  edges of obstacles are also lines of sight

## Slide 9: Visibility Graph Construction
repeat until done

## Slide 10: Visibility Graph Construction
the algorithm described is O(N 3) where N is the number of vertices