## Slide 1: Day 29
Geometric Dilution of Precision

## Slide 2: Trilateration
given two landmarks with known locations we can compute the two possible locations of the robot
  additional information will tell us which of the two locations (heading information, landmarks are on a wall, etc.)
landmark
d1
landmark
d2

## Slide 3: Trilateration
assume
  red landmark is located at the origin
  blue landmark is located a units along the x axis
then the robot is located at:
[0 0]T
d1
[0 a]T
d2

## Slide 4: Trilateration
if the distance measurements are noisy then there will be some uncertainty in the location of the robot

## Slide 5: Trilateration
notice that the uncertainty changes depending on where the robot is relative to the landmarks
uncertainty grows quickly if the robot is in line with the landmarks

## Slide 6: Trilateration
uncertainty grows as the robot moves farther away from the landmarks
  but not as dramatically as the previously slide

## Slide 7: Geometric Dilution of Precision
it many cases it might be nice to know how the uncertainty changes as a function of the robot position
  i.e., how much variation is there in the estimated position for some amount of variation in the distance measurements
    called the geometric dilution of precision
    where ΔX is the variation in the estimated pose (in this case, position) and ΔS is the variation in the sensor readings (in this case, distance)

## Slide 8: Geometric Dilution of Precision
if we take the limit as ΔS→0 then the GDOP is equal to the Jacobian of the measurement equation
*different than textbook
*positive root only

## Slide 9: Geometric Dilution of Precision
if the Jacobian is a square matrix, then we can examine its determinant
  the absolute value of the determinant tells you something about how much x and y will change
    the textbook calls the absolute value of the determinant the magnitude of J

## Slide 10: Geometric Dilution of Precision

## Slide 11: Geometric Dilution of Precision
the GDOP is very sensitive to changes in x along the y axis

## Slide 12: Geometric Dilution of Precision
the GDOP is less sensitive to changes in y along the x axis

## Slide 13: Geometric Dilution of Precision
simulated localization error

## Slide 14
similar problems appear in other research fields

## Slide 15: Registration Error
Suppose we have a tracked pointing stylus with a DRB having 4 fiducial markers.
model pointer

## Slide 16: Registration Error
actual pointer
Because the of measurement errors in the tracking system, the locations of the
fiducial markers cannot be measured exactly. The error between the actual and
measured marker locations is called the fiducial localization error (FLE).

## Slide 17: Registration Error
minimize : Σ ( FREi )2
actual pointer
When the model pointer is registered to the measured pointer, the FLE will
lead to some error in the estimated rotation and translation. The residual
errors in the fiducial locations after registration is called the fiducial registration
error (FRE).
model
pointer
fiducial registration
error ( FREi )

## Slide 18: Registration Error
target registration
error (TRE)
actual pointer
Usually, we are interested in points that are not fiducial locations. Any such
point (not used for registration purposes) is called a target. The error between
the true target position and registered target position is called the target
registration error (TRE).

## Slide 19: Analysis of TRE
TRE for different configurations of markers

## Slide 20: Anisotropic FLE
what happens if the DRB rotates about x-axis?

## Slide 21: Anisotropic FLE
TRE strongly dependent of rotation for anisotropic noise

## Slide 22: Why the Peak in TRE?
because rotational component of TRERMS is maximized when DRB faces the tracking camera

## Slide 23: Why the Peak in TRE?
and minimized when the DRB is perpendicular to the tracking camera

## Slide 24: Observed TRE
paradoxically, this behavior is exactly the opposite of what is observed in practice
  TRE is typically worse when the DRB is rotated away from the camera