## Slide 1: Case Study
Autonomous Cars

## Slide 2
Sebastian Thrun’s TED Talk describing Google’s driverless car
  www.ted.com/talks/sebastian_thrun_google_s_driverless_car.html

## Slide 3
Junior: The Stanford Entry in the Urban Challenge
  http://robots.stanford.edu/papers/junior08.pdf

## Slide 4: DARPA Urban Challenge
November 3, 2007
6 hours to complete a 96 km urban area course
multiple robotic vehicles carrying out missions on the same course at the same time
basic rules:
  stock vehicle
  obey California driving laws
  entirely autonomous
  avoid collisions with objects typical to urban environment
  must also be able to operate in parking lots
  DARPA supplied environment map with information on lanes, lane markings, stop signs, parking lots, and special checkpoints

## Slide 5: Junior

## Slide 6: Junior: Computation

## Slide 7: Junior: Sensors
Applanix POS LV 420 position and orientation system
  multiple GPS receivers, GPS heading measurement, inertial measurement, distance measurement, Omnistar Virtual Base Station
    position and orientation errors less than 100 cm and 0.1 degrees
2 side facing SICK LMS laser range finders
1 forward facing RIEGL LMS-Q120 laser range finder
1 roof mounted Velodyne HDL-64E laser range finder
2 rear mounted SICK LDLRS laser range finders
2 front mounted IBEO ALASCA XT laser range finders
5 BOSCH radars mounted in front grill

## Slide 8: Laser Obstacle Detection
challenging!
  curbs
  moving and static obstacles
  overhanging obstacles (tree branches, signs, etc.) that can be safely driven under

## Slide 9: Laser Obstacle Detection
primary sensor is the Velodyne laser range finder
  cannot reliably detect curb-sized obstacles near the vehicle because of self-occlusion

## Slide 10: Laser Obstacle Detection
curbs near the vehicle detected using the 2 front facing IBEO laser range finders and 2 rear facing SICK laser range finders
only obstacles close to the vehicle (5m in front and 15m in back) considered

## Slide 11: Static Mapping
discrete grid-based local maps based on laser scan data

## Slide 12: Static Mapping

## Slide 13: Dynamic Object Detection and Tracking
laser range scan data is mapped into a synthetic 2D scan of the environment

## Slide 14: Dynamic Object Detection and Tracking
areas of change are detected by comparing two synthetic scans taken over a short time interval
  if an obstacle in one scan falls in the freespace of the second scan then this is evidence of motion
new obstacle
absence of a previously seen obstacle

## Slide 15: Dynamic Object Detection and Tracking
particle filters are instantiated at each detected moving obstacle to track the object over time

## Slide 16: Dynamic Object Detection and Tracking
camera view

## Slide 17: Precision Localization
high precision GPS and inertial measurements are not sufficiently precise to achieve single lane localization in the DARPA supplied map
DARPA map is also inaccurate!
high precision localization within the lane is achieved using curb measurements and road reflectivity
  2 side facing SICK LMS and the forward facing RIEGL LMS-Q120 laser range finders pointed downward to measure infrared reflectivity change between road surface and painted lane markers
offsets greater than 1 m relative to GPS were common observed

## Slide 18: Precision Localization

## Slide 19: Global Path Planning
performed at each checkpoint and when a permanent road blockage is detected

## Slide 20: Global Path Planning
performed using dynamic programming on a discrete version of the map
cost function weights choices (which way to turn at an intersection, lane changes, etc.) probabilistically
  tends to perform lane changes earlier rather than later
  will avoid passing a slow moving car in the right lane if a right hand turn is up coming
  may decide against left hand turns at intersections if an alternate route is not much longer

## Slide 21: Road Navigation
global planner outputs a central path and also paths that have slight lateral shifts
  allows the vehicle to pass slower moving vehicles

## Slide 22: Freeform Navigation
used in parking lots and maneuvers such as U-turns
planning performed using a variation of A* called hybrid-A*

## Slide 23: Behavior Hierarchy
behavior governed by a finite state machine
not shown
*TRAFFIC_JAM
*ESCAPE

## Slide 24: Escaping Blockages
TRAFFIC_JAM and ESCAPE use hybrid-A* planner to find a path around road blockages

## Slide 25: Results
all 3 missions accomplished
55.96 miles in 4 hrs 5 mins 6 secs (22 km per hour)
  good for 2nd place
notable race events
  travel over a dirt road
  passing a disabled competitor
  avoiding a head on collision with a competitor driving partially in the wrong lane
  braking in reaction to an aggressive merge
  guilty of an aggressive merge
  guilty of pulling alongside a competitor stopped at a stop sign (mistaken for a parked car)