## Slide 1: Day 06
Horn's Method and Fiducial Registration Error

## Slide 2: Issues
the use of the least-squares criteria assumes
  identically distributed noise in each point
  isotropic noise in each point
    more accurate (although more complicated) algorithms are available if these criteria are not met
      Matei and Meer, IEEE PAMI, 28(10), Oct 2006

## Slide 3: Characterizing Error
most commonly used noise distribution is the zero-mean Gaussian (or normal) distribution
mean (location)
covariance (spread)

## Slide 4: Characterizing Error
in 1D
  standard deviation
  variance

## Slide 5: Characterizing Error
in 2D
  isotropic

## Slide 6: Characterizing Error
in 2D
  anisotropic

## Slide 7: Characterizing Error
in 2D
  anisotropic

## Slide 8: Characterizing Error
in 2D
  anisotropic

## Slide 9: Registration Error
Suppose we have a tracked pointing stylus with a DRB having 4 fiducial markers.
model pointer

## Slide 10: Registration Error
actual pointer
Because the of measurement errors in the tracking system, the locations of the
fiducial markers cannot be measured exactly. The error between the actual and
measured marker locations is called the fiducial localization error (FLE).

## Slide 11: Registration Error
minimize : Σ ( FREi )2
actual pointer
When the model pointer is registered to the measured pointer, the FLE will
lead to some error in the estimated rotation and translation. The residual
errors in the fiducial locations after registration is called the fiducial registration
error (FRE).
model
pointer
fiducial registration
error ( FREi )

## Slide 12: Registration Error
target registration
error (TRE)
actual pointer
Usually, we are interested in points that are not fiducial locations. Any such
point (not used for registration purposes) is called a target. The error between
the true target position and registered target position is called the target
registration error (TRE).

## Slide 13: Horn's Method and FLE
Horn's method (and all other ordinary least-squares methods) is optimal when FLE is identical and isotropic
{L}
{R}

## Slide 14: Horn's Method and TRE
early methods of studying the behaviour of TRE relied on simulation studies
    IEEE Transactions on Medical Imaging, vol. 16, no. 4, Aug. 1997
Given a set of registration points {P} = {p0, p1, ..., pn-1}, a target point t, and an FLE variance s 2:
define noise

## Slide 15: Horn's Method and TRE
repeat 10,000 times
  create a noise copy {Q} of {P} where
  register {Q} to {P} using Horn's method to obtain the rotation Rj and translation dj
  compute the registered target location
  compute the squared TRE
compute the root mean squared (RMS) TRE

## Slide 16: Horn's Method and TRE
simulations performed for different configurations of markers

## Slide 17: Horn's Method and TRE

## Slide 18: Horn's Method and TRE
simulation of TRE vs FLE

## Slide 19: Horn's Method and TRE
simulation of TRE vs number of markers

## Slide 20: Horn's Method and TRE
summary of results:
  TRE depends strongly on configuration of markers
  TRE2
  TRE2

## Slide 21: Analysis of TRE
Fitzpatrick, West, and Maurer Jr performed a statistical analysis of fiducial registration (assuming identical isotropic FLE)
    IEEE Transactions on Medical Imaging, vol. 17, no. 5, Oct 1998
  t target location
  n number of markers
  d k distance between the target and the k th principal axis
  f k RMS distance between the fiducials and the k th principal axis

## Slide 22: Analysis of TRE
TRE for different configurations of markers

## Slide 23: Analysis of TRE
TRE versus FLE

## Slide 24: Analysis of TRE
other interesting results
  FRE is independent of the marker configuration!
  if you compute the TRE for the fiducial markers you get
    i.e., a small FRE implies a large TRE at the marker location!
    FRE is poor indicator of registration quality