## Slide 1: Day 07
Horn's Method and Fiducial Localization Error

## Slide 2: Horn's Method and FLE
Horn's method (and all other ordinary least-squares methods) is optimal when FLE is identical and isotropic
{L}
{R}

## Slide 3: Anisotropic FLE
in most optical tracking systems, measurement error is largest along the viewing direction
{L}
{R}

## Slide 4: Anisotropic FLE
what happens if the DRB rotates about x-axis?

## Slide 5: Isotropic FLE
TRE independent of rotation for isotropic noise

## Slide 6: Anisotropic FLE
TRE strongly dependent of rotation for anisotropic noise

## Slide 7: Why the Peak in TRE?
because rotational component of TRERMS is maximized when DRB faces the tracking camera

## Slide 8: Why the Peak in TRE?
and minimized when the DRB is perpendicular to the tracking camera

## Slide 9: Observed TRE
paradoxically, this behavior is exactly the opposite of what is observed in practice
  TRE is typically worse when the DRB is rotated away from the camera

## Slide 10: Heteroscedastic FLE
in reality, noise in each point almost certainly comes from different distributions
{L}

## Slide 11: Heteroscedastic FLE
furthermore, both sets of measured points almost certainly contain noise
{R}

## Slide 12: Heteroscedastic FLE
Estimation of nonlinear errors-in-variables models for computer vision applications. IEEE Trans. Pattern Anal. Machine Intell. , 28, 1537-1552, 2006.
arguably better is Matei's PhD dissertation
  http://coewww.rutgers.edu/riul/research/theses/abstract/matei_thesis.html
    ellipse fitting
    fundamental matrix estimation
    absolute orientation estimation
    camera calibration
    trifocal tensor estimation

## Slide 13: HEIV Algorithm for Absolute Orientation
Compute the matrices Zi (one for each registration point) from the original noisy measurements
Compute the covariances of the carriers.
Use Horn's method to obtain an estimate of the solution.
Use the HEIV algorithm to obtain an estimate of the quaternion (encodes rotation) and intercept (encodes the translation)
Recover the rotation matrix (from the quaternion) and the translation (from the intercept)

## Slide 14: Day 07
Shape-based Registration

## Slide 16
find rotation and translation that best matches (registers) the points to the surface
batch process
  how many points?
  where are the best points?
  how do you improve a registration?
  how good is the registration?
model
registered
patient points
Pn = {pi=1..n}
{L}
{R}

## Slide 17: Relationship to Absolute Orientation
notice that the shape registration problem is similar to the absolute orientation problem
  the important difference is that we do not know the point correspondences
    i.e., we do not know which surface point xi corresponds to registration point pi
if we did know the correspondences then the problem is solved; just use any solution to the absolute orientation problem

## Slide 18: ICP Algorithm
iterated closest point algorithm
  Besl and McKay. IEEE Transactions on Pattern Analysis and Machine Intelligence, vol. 14, no. 2, Feb 1992.
  solves for the rotation and translation that best aligns a set of points to a surface
    surface can have any representation that allows for a point-to-surface distance computation

## Slide 19: ICP Algorithm
Find an initial guess for the rotation R and translation d.
Apply R and d to P to obtain Q0 = {q1, ..., qn}
For k = 1, 2, ....
  Find the points on the surface Yk = {y1, ..., yn} closest to Qk-1.
  Use Horn's method to match P to Yk; this yields the new estimate for R and d.
  Apply R and d to P to obtain Qk = {q1, ..., qn}
  Compute the mean squared error
Until for some threshold value