## Slide 1: Day 10
Statistical Robustness

## Slide 2: RANSAC
best_model = {}
best_consensus_set = {}
best_error = infinity
for i = 1..MAX_ITERATIONS inlier_set = randomly selected subset of data
remainder_set = data with inlier_set removed
consensus_set = inlier_set
inlier_model = fit inlier_set to model
for each element in remainder_set
if element fits inlier_model then add it to consensus_set
end for
if |consensus_set| > MIN_CONSENSUS_SIZE
consensus_model = fit consensus_set to model
consensus_error = residual error of consensus_model
if consensus_error < best_error
best_model = consensus_model
best_consensus_set = consensus_set
best_error = consensus_error
end if
end if
end for

## Slide 3: LMS
best_model = {}
best_error = infinity
for each subset X of size p of the data
X_model = fit X to model (uses p data points)
X_error = median residual (over all N data points)
if X_error < best_error
best_model = X_model
best_error = X_error
end if
end for

## Slide 4: Outlier Detection
LMS produces robust but sub-optimal estimates
  better estimates can be obtained by using LMS to obtain an estimate, removing the outlying data points, and then computing a least-squares estimates from the cleaned data set
outliers can be identified using a priori knowledge (if you have it)
  e.g., using Horn’s method with a typical optical tracking system it would be reasonable to expect inliers to have an FRE < 1mm
can also obtain a robust estimate of scale and label a data point as an outlier if its squared residual error is greater than some constant times the squared scale estimate
  P.J. Rousseeuw and A.M. Leroy. Robust Regression and Outlier Detection. John Wiley & Sons, New York, 1987.