## Slide 1: Day 21
Kalman Filter Examples

## Slide 2: Tank of Water
static level
plant model
measurement model

## Slide 3: Tank of Water
filling at a (noisy) constant rate and we do not care about the rate
ut is the change in the water level that occurred from time t-1 to t
plant model
measurement model

## Slide 4: Tank of Water
filling at a (noisy) constant rate and we want to estimate the rate
plant model
measurement model

## Slide 5: Projectile Motion
projectile launched from some initial point with some initial velocity under the influence of gravity (no drag)

## Slide 6: Projectile Motion
convert the continuous time equations to discrete recurrence relations for some time step

## Slide 7: Projectile Motion
rewrite in matrix form

## Slide 8: Omnidirectional Robot
an omnidirectional robot is a robot that can move in any direction (constrained in the ground plane)
  http://www.youtube.com/watch?v=DPz-ullMOqc
  http://www.engadget.com/2011/07/09/curtis-boirums-robotic-car-makes-omnidirectional-dreams-come-tr/
if we are not interested in the orientation of the robot then its state is simply its location

## Slide 9: Omnidirectional Robot
a possible choice of motion control is simply a change in the location of the robot
with noisy control inputs

## Slide 10: Differential Drive
recall that we developed two motion models for a differential drive
  using the velocity model, the control inputs are

## Slide 11: Differential Drive
using the velocity motion model the discrete time forward kinematics are
Eqs 5.9

## Slide 12: Differential Drive
there are two problems when trying to use the velocity motion model in a Kalman filter
  the plant model is not linear in the state and control
  it is not clear how to describe the control noises as a plant covariance matrix

## Slide 13: Measurement Model
there are potentially other problems
  any non-trivial measurement model will be non-linear in terms of the state
consider using the known locations of landmarks in a measurement model

## Slide 14: Landmarks
a landmark is literally a prominent geographic feature of the landscape that marks a known location
in common usage, landmarks now include any fixed easily recognizable objects
  e.g., buildings, street intersections, monuments
for mobile robots, a landmark is any fixed object that can be sensed

## Slide 15: Landmarks for Mobile Robots
visual
  artificial or natural
retro-reflective
beacons
  LORAN (Long Range Navigation): terrestrial radio; now being phased out
  GPS: satellite radio
acoustic
scent?

## Slide 16: Landmarks: RoboSoccer

## Slide 17: Landmarks: Retroreflector

## Slide 18: Landmarks: Active Light

## Slide 19: Trilateration
uses distance measurements to two or more landmarks
suppose a robot measures the distance d1 to a landmark
  the robot can be anywhere on a circle of radius d1 around the landmark
landmark
d1

## Slide 20: Trilateration
without moving, suppose the robot measures the distance d2 to a second landmark
  the robot can be anywhere on a circle of radius d2 around the second landmark
landmark
d1
landmark
d2

## Slide 21: Trilateration
the robot must be located at one of the two intersection points of the circles
  tie can be broken if other information is known
landmark
d1
landmark
d2

## Slide 22: Trilateration
if the distance measurements are noisy then there will be some uncertainty in the location of the robot

## Slide 23: Trilateration
notice that the uncertainty changes depending on where the robot is relative to the landmarks
uncertainty grows quickly if the robot is in line with the landmarks

## Slide 24: Trilateration
uncertainty grows as the robot moves farther away from the landmarks
  but not as dramatically as the previously slide

## Slide 25: Triangulation
triangulation uses angular information to infer position
  http://longhamscouts.org.uk/content/view/52/38/

## Slide 26: Triangulation
in robotics the problem often appears as something like:
  suppose the robot has a (calibrated) camera that detects two landmarks (with known location)
    then we can determine the angular separation, or relative bearing, α between the two landmarks
α
known
position
known
position
unknown
position
D1
Z2
Z1

## Slide 27: Triangulation
the unknown position must lie somewhere on a circle arc
  Euclid proved that any point on the shown circular arc forms an inscribed triangle with angle α
    we need at least one more beacon to estimate the robot’s location
α
known
position
known
position
D1
α