## Slide 1: Day 33
Range Sensor Models

## Slide 2: Beam Models of Range Finders
given the map and the robot’s location, find the probability density that the range finder detects an object at a distance along a beam
the k is here because range sensors typically return many measurements at one time; e.g., the sensor might return a full 360 degree scan made up of K measurements at once

## Slide 3: Beam Models of Range Finders
most range finders have a minimum and maximum range
we seek a model that can represent
  the correct range measurement with noise
  unexpected obstacles
  failures
  random measurements
1
2
3

## Slide 4: Beam Models of Range Finders
beam-based model is computationally expensive
  each measurement requires a ray intersection with the map to compute
Velodyne HDL-64E S2 >1.3 million measurements per second

## Slide 5: Beam Models of Range Finders
computational expense can be reduced by precomputing
  decompose state space into a 3D grid
    much like histogram filter
  for each grid location compute and store
much faster than ray casting but…

## Slide 6: Beam Models of Range Finders
changes abruptly for small changes in
  especially true for small changes in θ
map obstacle detected for robot bearing θ
map obstacle missed for robot bearing θ+d θ

## Slide 7: Likelihood Fields for Range Finders
an alternative model called likelihood fields overcomes the limitations of the beam model
  but is not physically meaningful
recall that a range measurement is a distance measured relative to the robot
  can we transform into a point in the map?

## Slide 8: Likelihood Fields for Range Finders
measured in {1}
measured in {0}
want this in {0}

## Slide 9: Likelihood Fields for Range Finders

## Slide 10: Likelihood Fields for Range Finders
similar to the beam model, we assume 3 types of sources of noise and uncertainty
correct measurement with noise
failures
random measurements

## Slide 11: Likelihood Fields for Range Finders
Correct Measurement with Noise
once we have we find the point on an obstacle in the map that is nearest to and compute the distance d between those two points
this measurement is modeled as a zero-mean Gaussian with variance

## Slide 12: Likelihood Fields for Range Finders

## Slide 13: Beam Models of Range Finders
Failures
range finders can fail to sense an obstacle in which case most sensors return
modeled as a point mass distribution centered at

## Slide 14: Beam Models of Range Finders
Random Measurements
unexplainable measurements are modeled as a uniform distribution over the range [0, ]

## Slide 15: Beam Models of Range Finders
the complete model is a weighted sum of the previous three densities with weights

## Slide 16: Beam Models of Range Finders