## Slide 1: Day 05
Horn's Method

## Slide 2: Frames in Computer-Aided Surgery
{C}
{P}
{T}

## Slide 3: Frames in Computer-Aided Surgery
{P}
{T}
{M}

## Slide 4: Frames in CGI

## Slide 5: Frames in Computer-Aided Surgery
{CT }
{P}

## Slide 6: Fiducial Registration
physical markers easily locatable in the medical imagery and on the patient are often used in neurosurgery to establish the spatial relationship between the patient and the images
same fundamental problem appears in many different fields and goes by many different names
  fiducial registration
  point-based registration
  paired-point registration
  registration with correspondances
  absolute orientation
  point fitting
  ...

## Slide 7: Problem Statement
given n points measured in {L} and {R} estimate the transformation (or )
{L}
{R}

## Slide 8: Problem Statement
given n points measured in {L} and {R}
find the transformation
residual errors
find the least-squares solution

## Slide 9: 1. Compute the Centroids
compute and subtract centroids from both sets of measurements

## Slide 10: 2. Compute the Matrix M
compute the sum of the component products for all pairs of corresponding points

## Slide 11: 3. Compute the Matrix N
use the elements of M to compute N
  note that N is symmetric

## Slide 12: 4. Compute Eigenvectors and Eigenvalues
compute the eigenvectors and eigenvalues of N
  in principle, the eigenvectors and eigenvalues can be found by finding the roots of a 4th order polynomial but numeric methods are easier
    the fact that N is symmetric allows for efficient numeric eigenvalue/vector solvers
    in Matlab
% D is a diagonal matrix of eigenvalues
% columns of V are the corresponding eigenvectors
[V, D] = eig(N);

## Slide 13: 5. Find the Quaternion
the quaternion representing the estimated rotation is the eigenvector corresponding to the largest positive eigenvalue
    in Matlab
% y is the largest eigenvalue
% idx is the index of y in diag(D)
[y, idx] = max(diag(D));
Q = V(:, idx);

## Slide 14: Quaternions
unit quaternions are another representation of rotations (and orientations)
the unit quaternion Q can be thought of as a scalar qw and a vector [qx qy qz]T

## Slide 15: 6. Compute the Translation
use the centroids to compute the estimated translation
  recall that
  using the centroids

## Slide 16: Issues
the use of the least-squares criteria assumes
  identically distributed noise in each point
  isotropic noise in each point
    more accurate (although more complicated) algorithms are available if these criteria are not met
      Matei and Meer, IEEE PAMI, 28(10), Oct 2006

## Slide 17: Issues
inaccurate measurements (statistical outliers) will lead to a poor estimate of the transformation
measured
registered
4 perfect measurements
1 inaccurate
measurement