## Slide 1: DICOM

## Slide 2: DICOM
set of standards developed shortly after commercial CT machines started becoming available (early 1980s)
  in part to allow access to image data by people other than the manufacturers
intent
  promote communication of digital image information, regardless of device manufacturer
  facilitate the development and expansion of picture archiving and communication systems (PACS) that can also interface with other systems of hospital information
  allow the creation of diagnostic information data bases that can be interrogated by a wide variety of devices distributed geographically

## Slide 3: DICOM
brochure
http://medical.nema.org/standard.html

## Slide 4: DICOM in Matlab
functionality provided via the Image Processing toolbox
  http://www.mathworks.com/help/images/index.html
  http://www.mathworks.com/help/images/scientific-file-formats.html
there is a lot of confidential information embedded in a DICOM image
  Supplement 55 Attribute Level Confidentiality (including De-identifiation)
  dicomanon

## Slide 5: Viewing Medical Images
for many types of medical images there is a mismatch between the range of the image data and the range of values that can be displayed
  CT range = -1024 to 3072
  8-bit grayscale = 256 gray levels
need to map the image data range to display range
  “window” and “level” in medical imaging
  http://blogs.mathworks.com/steve/2006/02/17/all-about-pixel-colors-window-level/

## Slide 6: Viewing Medical Images
modern imaging workstations support volume rendering of 3D images
  http://www.fovia.com/galleryhome.php
not a graphics course, but…
  http://en.wikipedia.org/wiki/Volume_rendering
  http://en.wikipedia.org/wiki/Volume_ray_casting
  Real-Time Volume Graphics
  Visualization in Medicine: Theory, Algorithms, and Applications

## Slide 7: Segmentation

## Slide 9: Segmentation
divide an image into parts that correspond to salient regions (e.g., objects or parts of objects)
complete segmentation
  produces a set of S disjoint regions Ri corresponding uniquely with objects in the image
partial segmentation
  regions do not correspond directly to objects in the image

## Slide 10: Segmentation
segmentation is task dependent
  the whole organ?
  all of the parts of the organ?
  a specific part of the organ?
  unusual regions?

## Slide 11: Bottom-up versus Top-down
bottom-up segmentation
  no prior knowledge of what objects are in the scene
    segmentation into homogeneous regions
  unlikely to produce a complete segmentation except in simple cases
top-down segmentation
  objects in the image are recognized (using a detector) and then segmented
  uses prior knowledge of object classes to guide segmentation

## Slide 12: Approaches to Segmentation
thresholding
  usually intensity-based
edges
  edge detection followed by edge grouping to find boundaries separating regions
regions
  individual regions are found directly by region growing, splitting, and merging

## Slide 13: Thresholding
global intensity thresholding is the simplest segmentation process
input image f(i, j), output image g(i, j) for each pixel (i, j)
works only if the objects in the image are distinct from the background intensity

## Slide 14: Thresholding
original
good threshold
threshold too low
threshold too high

## Slide 15: Threshold Detection
a histogram of intensity values can be helpful in selecting a threshold value

## Slide 16: Optimal Thresholding
histogram is treated as the sum of two or more probability densities
  choose threshold to minimize segmentation error

## Slide 17: Optimal Thresholding

## Slide 18: Edge-based Segmentation
edge-based segmentation tries to find the borders separating regions
edges are found using an edge detector
  detected edges usually do not form closed borders
  detectors can miss weak edges
  detectors can find too many edges

## Slide 19: Edge
an edge is a discontinuity in image intensity along one direction
edges in real images are often blurry and noisy

## Slide 20: Edge Detection Kernels
discrete approximations to first derivative
  attempt to compute the image gradient magnitude
Roberts Cross
Prewitt
Sobel