## Slide 1: Region-Based Segmentation
the basic idea
  divide image into zones of maximum homogeneity
  for some homogeneity measure H()
homogeneity can be computed based on
  intensity
  color (not usually applicable in medical imaging)
  texture
  shape

## Slide 2: Region Merging
a possible approach
  assume every pixel is a region and merge pixels based on similarity
alternatively
  oversegment the image into regions and merge regions
partition image into regions
form region adjacency graph (RAG)
for each region
  consider its adjacent region and test for homogeneity
  if then merge the regions and update the RAG
repeat step 3 until no regions are merged

## Slide 3: Region Merging
simple homogeneity test
  compare mean region intensities and merge if the intensities are within a threshold distance
  has the same problems as other threshold approaches

## Slide 4: Region Merging
homogeneity test as hypothesis testing
  assume or estimate a statistical distribution of the pixel intensities over a region and use a statistical hypothesis test
  H0: Both regions are the same (the pixel intensities come from the same distribution)
  H1: Both regions are different (the pixel intensities come from different distributions)

## Slide 5: Region Merging
homogeneity test as hypothesis testing example
  if we assume that pixel intensities are Gaussian distributed
  if we assume pixel intensities are independent then the joint probability density under the null hypothesis is

## Slide 6: Region Merging
homogeneity test as hypothesis testing example (cont)
  if we assume pixel intensities are independent then the joint probability density under the null hypothesis is
  the likelihood ratio is
  if L is below a threshold value then merge the two regions

## Slide 7: Watershed Segmentation
topographic map of High Park

## Slide 8: Watershed Segmentation
watershed segmentation models the image as a topographic landscape with the pixel intensities representing elevation
there are 3 kinds of points
  local minima
  points where a drop of water would fall to a single local minima
    “catchment basins”
  points where a drop of water would be equally likely to fall into more than one minima
    “watersheds”

## Slide 9: Watershed Segmentation

## Slide 10: Watershed Segmentation
regions boundaries are the watersheds
to find the watersheds
  fill the catchment basins with water starting from the local minima
  if two catchment basins would merge by adding a little more water then build a dam between the two basins
    the dams are the watersheds

## Slide 11: Watershed Segmentation
http://cmm.ensmp.fr/~beucher/wtshed.html
http://www.mathworks.com/products/demos/image/watershed/ipexwatershed.html
Jean Cousty, Gilles Bertrand, Laurent Najman, and Michel Couprie. Watershed Cuts: Minimum Spanning Forests and the Drop of Water Principle. IEEE Transactions on Pattern Analysis and Machine Intelligence. 31 (8). August 2009. pp. 1362–1374.

## Slide 12: Segmentation via Non-rigid Registration
suppose that you have a contour (defined by a set of points) of a shape
  can we transfer the contour onto an image by finding the corresponding set of points on the image?

## Slide 13
given n corresponding control points find functions f and g such that

## Slide 14: Polynomial Transformation
we might choose functions f and g to be polynomials in x and y
this is easy to solve in a least-squares way

## Slide 15: Polynomial Transformation

## Slide 16: Thin Plate Spline
Goshtasby, IEEE Transactions on Geoscience and Remote Sensing, 26(1), Jan 1988.
undeformed rubber sheet
deformed rubber sheet (pulled at edges)

## Slide 17: Thin Plate Spline
using 20 control points
thin plate spline
polynomial (degree 2)

## Slide 18: Thin Plate Splines
source image
target image

## Slide 19
centrally located control points

## Slide 20
warped image
difference between warped
and target images

## Slide 21
control points located at periphery

## Slide 22
warped image
difference between warped
and target images

## Slide 24: Thin Plate Spline
the surface of an infinite plate loaded with point loads is called a surface spline and is given by where and (xj, yj) is the position of the jth point load

## Slide 25: Thin Plate Spline
the coefficients Fj must meet certain constraints
the constraints are related to the original integral equation that the thin plate spline minimizes

## Slide 26: Thin Plate Spline
by choosing
and imposing the constraints
we can solve a linear system of
equations to compute the
thin plate spline