## Slide 1: CSE4421/5324: Introduction to Robotics

## Slide 2: Contact Information
Burton Ma Lassonde 2046 burton@cse.yorku.ca
CSE4421/5324 lectures Monday, Wednesday, Friday 2:30-3:30PM (ACW305) labs Thursday 11:30-1:30, Prism 1006B www.cse.yorku.ca/course/4421 (web site not complete yet)

## Slide 3: Graduate Studies in Computer Science & Engineering
York University

## Slide 4: Why a Master’s degree?
Job titles: Computer systems analyst, computer programmer, computer scientist, computer systems designer
Bachelor's degree salary: $50,985
Master's degree salary : $72,515
  Source: http://msn.careerbuilder.com/Article/MSN-1817-Salaries-and-Promotions-Bachelors-vs-Masters-How-Does-Your-Salary-Stack-Up/

## Slide 5: But I can’t afford grad school …

## Slide 6: We’ll pay you to study
$25,000 / year
Many will be awarded an entrance scholarship of $6,000 on top of the above $25,000.
Excellent applicants will be awarded an entrance scholarship of $10,000 on top of the above $25,000.

## Slide 7: What will I do for my Master’s?
5 terms (20 months) of full-time study
Complete 5 courses (15 credits) with a GPA of at least B+
Complete a research project and write and successfully defend a thesis
Work as a TA (conducting labs/tutorials, marking, lab monitoring)
Have fun (ski trips, movie nights, foosball tournaments, Halloween/Christmas parties, conferences, etc.)

## Slide 8: How good am I to be admitted?
An undergraduate honours degree in Computer Science or Computer Engineering
Minimum GPA of B+ in the last 2 years of study
Research aptitude (just as important as GPA)
The above requirements are minimum requirements and do not guarantee admission

## Slide 9: Research Aptitude
Take project courses: CSE4080, CSE4081, CSE4082, CSE4083, CSE4084, CSE4090
To find out if you are good at doing research
To get to know professors (potential future supervisors and/or referees)
To find a suitable research area/topic for your Master’s thesis

## Slide 10: How to Apply?
Online applications only
http://futurestudents.yorku.ca/graduate/programs/computer-science-and-engineering
http://futurestudents.yorku.ca/graduate/programs/computer-engineering
Deadline: January 16, 2013 for 2013-14 admission
We accept late applications until February 18. Email Ms. Ouma Paul Gill (gradasst@cse.yorku.ca) for permission to apply late.

## Slide 11: A little investment goes a long way …
Bachelor's degree salary : $50,985
Master's degree salary : $72,515

## Slide 12: For more information …
Information session: Friday, January 11, 2:30-3:30
Location: LAS-3033 (Comp Sci & Eng Building)
Web: www.cse.yorku.ca/grad/faq.html
E-mail:
  Graduate program assistant: Ouma Paul Gill gradasst@cse.yorku.ca
  Graduate program director: U. T. Nguyen utn@cse.yorku.ca

## Slide 13: General Course Information
The course introduces the basic concepts of robotic manipulators and autonomous systems. After a review of some fundamental mathematics the course examines the mechanics and dynamics of robot arms, mobile robots, their sensors and algorithms for controlling them.
two robotic arms
everything in Matlab (and some Java?)
required textbook
  Thrun, Burgard and Fox, Probabilistic Robotics, The MIT Press, 2006
other references
  see course web page

## Slide 14: Labs
six 2-hour labs
  Thursday 11:30-1:30 in Prism CSEB1006B
  different lab sections alternate between weeks
    except for Lab 01!
  first part of Lab 01 already posted and must be completed prior to lab

## Slide 15: Assessment
labs
assignments
midterm
exam
independent learning module?

## Slide 16: A150 Robotic Arm
link 3
link 2

## Slide 17: Kinematics
the study of motion that ignores the forces that cause the motion
  “geometry of motion”
interested in position, velocity, acceleration, etc. of the various links of the manipulator
  e.g., where is the gripper relative to the base of the manipulator? what direction is it pointing in?
  described using rigid transformations of the links

## Slide 18: Kinematics
forward kinematics:
  given the link lengths and joint angles compute the position and orientation of the gripper relative to the base
    for a serial manipulator there is only one solution
inverse kinematics:
  given the position (and possibly the orientation) of the gripper and the dimensions of the links, what are the joint variables?
    for a serial manipulator there is often more than one mathematical solution

## Slide 19: Wheeled Mobile Robots
robot can have one or more wheels that can provide
  steering (directional control)
  power (exert a force against the ground)
an ideal wheel is
  perfectly round (perimeter 2πr)
  moves in the direction perpendicular to its axis

## Slide 20: Wheel

## Slide 21: Deviations from Ideal

## Slide 22: Differential Drive
two independently driven wheels mounted on a common axis

## Slide 23: Forward Kinematics
for a robot starting with pose [0 0 0]T moving with velocity V(t) in a direction θ(t) :

## Slide 24: Sensitivity to Wheel Velocity
σ = 0.05
σ = 0.01

## Slide 25: Localization using Landmarks: RoboSoccer

## Slide 26: Maps
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | *
* |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
start
goal

## Slide 27: Path Finding
start
goal

## Slide 28: Localization
start
goal

## Slide 29: EKF SLAM Application
[MIT B21, courtesy by John Leonard]
www.probabilistic-robotics.org

## Slide 30: EKF SLAM Application
raw odometry
estimated trajectory
[courtesy by John Leonard]
www.probabilistic-robotics.org