## Slide 1: Day 27-28
Non-parametric Filters

## Slide 2: Localizing a Robot in a Hallway
consider a robot moving down a hall equipped with a sensor that measures the presence of a door beside the robot
  the pose of the robot is simply its location on a line down the middle of the hall
  the robot starts out knowing how far down the hallway it is located
    Kalman-like filters require an initial estimate of the location
  robot has a map of the hallway showing it where the doors are

## Slide 3: Kalman Localization
robot starts out knowing how far down the hallway it is located

## Slide 4: Kalman Localization
as the robot moves forward, its uncertainty in its location shifts and grows according to its motion model

## Slide 5: Grid Localization
when it reaches a door, it can incorporate this measurement into its state estimate
measurement liklihood
updated state estimate

## Slide 6: Grid Localization
as the robot moves forward, its uncertainty in its location shifts and grows according to its motion model

## Slide 7: Gaussian Assumption
Kalman-like filters assume that quantities can be represented accurately as a mean + covariance
  e.g., the state is a random variable with Gaussian distribution
  e.g., measurements are random variables with Gaussian distribution

## Slide 8: Gaussian Assumption
assumption is ok here
EKF
UKF

## Slide 9: Gaussian Assumption
assumption is (possibly) not ok here
EKF
UKF

## Slide 10: Gaussian Assumption
assumption is not ok here
p(x | robot is sensing a door)

## Slide 11: Non-parametric Filters
non-parametric filters do not rely on a fixed functional form of the state posterior
instead, they represent the posterior using a finite number of values each roughly corresponding to a region (or point) in state space
two variations
  partition state space into a finite number of regions
    e.g., histogram filter
  represent the posterior using a finite number of samples
    e.g., particle filter

## Slide 12: Histogram
bins
“table of frequencies”

## Slide 13: Histogram Filter
histogram filter uses a histogram to represent probability densities
in its simplest form, the domain of the densities is divided into subdomains of equal size with each subdomain being a bin of the histogram
  the value stored in the bin is proportional to the density

## Slide 14: Histogram Filter
suppose the domain of the state x is [-5, 5] and that x is a random variable with Gaussian density (mean 0, variance 1)
  using bins of width w = 0.1 we can represent the density using the following histogram
x
height of bar
center of bin i
Gaussian PDF
histogram p

## Slide 15: Histogram Filter
suppose we want to pass the density through some non-linear function
reminder: this is the solution obtained
by passing 500,000 random samples
through f (x), not the result of using a
histogram filter

## Slide 16: Histogram Filter
create an empty histogram h with bins xc,i
for each i
  yi = f (xc,i)
  ni = p(xc,i)
  find the bin bk that yi belongs in
  h (bk) = h (bk) + ni

## Slide 17: Histogram Filter
alternatively
create an empty histogram h with bins xc,i
for each bin bk
probability that yi is in bin bk

## Slide 18: Histogram Filter

## Slide 19: Grid Localization
grid localization uses a histogram filter over a grid decomposition of pose space
consider a robot moving down a hall equipped with a sensor that measures the presence of a door beside the robot
  the pose of the robot is simply its location on a line down the middle of the hall
  the robot starts out having no idea how far down the hallway it is located
  robot has a map of the hallway showing it where the doors are
  grid decomposes the hallway into a finite set of non-overlapping intervals
    e.g., every 50cm would yield intervals [0, 0.5], (0.5, 1], (1, 1.5], …

## Slide 20: Grid Localization
the robot starts out having no idea how far down the hallway it is located
  the histogram of its state density is uniform

## Slide 21: Grid Localization
because the robot is beside a door, it has a measurement
  it can incorporate this measurement into its state estimate
measurement liklihood
updated state estimate

## Slide 22: Grid Localization
as the robot moves forward, its uncertainty in its location shifts and grows according to its motion model

## Slide 23: Grid Localization
when it reaches a door, it can incorporate this measurement into its state estimate
  it now has a pretty good idea where it is in the hallway
measurement liklihood
updated state estimate

## Slide 24: Grid Localization
as the robot moves forward, its uncertainty in its location shifts and grows according to its motion model

## Slide 25: Grid Localization Algorithm
algorithm_grid_localization( )
for all k do
motion_model( )
measurement_model( )
endfor
return
histogram
control input
measurement
map
center of mass of grid cell xi