## Slide 1: Day 29
Bug Algorithms

## Slide 2: Fundamental Problems
Chapter 2 of Dudek and Jenkin begins:
  "Before delving into the harsh realities of real robots...“
lists 5 fundamental problems
  path planning
  localization
  sensing or perception
  mapping
  simultaneous localization and planning

## Slide 3: A Point Robot
represents a mobile robot as a point in the plane*
the point P fully describes the state of the robot
  called pose or configuration
robot motion causes the state to change

## Slide 4: Free Space and Obstacles
the set of valid poses is called the free space Cfree of the robot
the invalid poses are obstacles
obstacle
obstacle
obstacle
obstacle
freespace
point
robot
obstacle

## Slide 5: Path Planning
is it possible for the robot to move to a goal configuration while remaining in Cfree ?
obstacle
obstacle
obstacle
obstacle
freespace
start
obstacle
goal

## Slide 6: Path Planning Using Bugs
bug algorithms assume:
  point robot
  known goal location
  finite number of bounded obstacles
  robot can perfectly sense its position at all times
  robot can compute the distance between two points
  robot can remember where it has been
  robot can perfectly sense its local environment
  robot can instantaneously change direction

## Slide 7: Bug Zero
assumes a perfect contact sensor
repeat
  head towards goal
  if goal is reached then stop
  if an obstacle is reached then follow the boundary until heading towards the goal is again possible

## Slide 8: Bug Zero
obstacle
obstacle
obstacle
obstacle
freespace
start
obstacle
goal
a right turning bug

## Slide 9: Bug Zero
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 10: Bug Zero
not guaranteed to reach the goal
obstacle
goal
start
gets stuck here because
as soon as it moves down
there is a path to the goal
that does not go through
the obstacle

## Slide 11: Bug One
assumes a perfect contact sensor
repeat:
  head toward goal T
  if goal is reached then stop
  if an obstacle is reached then
    remember the point of first contact H (the hit point)
    follow the boundary of the obstacle until returning to H and remember the point L (the leave point) closest to T from which the robot can depart directly towards T
      if no such point L exists then the goal is unreachable; stop
    move to L using the shortest boundary following path

## Slide 12: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 13: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
L

## Slide 14: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
L

## Slide 15: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 16: Bug Two
Bug Two uses a line, called the m-line, from the start point to the goal
  sometimes called the direct path
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
m-line, or direct path

## Slide 17: Bug Two
assumes a perfect contact sensor
repeat:
  head toward goal T along the m-line
  if goal is reached then stop
  if an obstacle is reached then
    remember the point of first contact H (the hit point)
    follow the boundary of the obstacle until the m-line is crossed at a leave point closer to the goal than H
      if no such point L exists then the goal is unreachable; stop
    leave the obstacle and head toward T

## Slide 18: Bug Two
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
m-line, or direct path

## Slide 19: Bug Two

## Slide 20: Bug One versus Bug Two
Bug One uses exhaustive search
  it considers all leave points before leaving the obstacle
Bug Two uses greedy search
  it takes the first leave point that is closer to the goal

## Slide 21: Sensing the Environment
Bug1 and Bug2 use a perfect contact sensor
we might be able to achieve better performance if we equip the robot with a more powerful sensor
a range sensor measures the distance to an obstacle; e.g., laser range finder
  emits a laser beam into the environment and senses reflections from obstacles
  essentially unidirectional, but the beam can be rotated to obtain 360 degree coverage
  http://velodynelidar.com/lidar/lidar.aspx

## Slide 22: Tangent Bug
assumes a perfect 360 degree range finder with a finite range
  measures the distance r(x, q) to the first obstacle intersected by the ray from x with angle q
  has a maximum range beyond which all distance measurements are considered to be r = 
the robot looks for discontinuities in r(x, q)

## Slide 23: Tangent Bug
O1
O2
O3
O4
O5
O6

## Slide 24: Tangent Bug
currently, bug thinks goal is reachable so it moves toward the goal
  called “motion to goal” mode
goal

## Slide 25: Tangent Bug
once the obstacle is sensed, the bug needs to decide how to navigate around the obstacle
move towards the sensed point Oi that minimizes the distance d(x, Oi) + d(Oi, qgoal) (called the heuristic distance)
goal
O1

## Slide 26: Tangent Bug

## Slide 27: Tangent Bug

## Slide 28: Tangent Bug
problem with concave obstacles
  eventually the robot reaches a point where d(x, Oi) + d(Oi, qgoal) starts to increase
  once this happens, the robot switches to “boundary following” mode

## Slide 29: Tangent Bug
trick here is that the robot remembers the distance dfollowing between M and qgoal
  M is the point on the blocking obstacle that had the shortest distance to the goal when the heuristic distance started to increase

## Slide 30: Tangent Bug
the robot returns to “motion to goal” mode as soon as it reaches a point where the distance between a sensed point and the goal or the distance between the robot location and the goal is less than dfollowing

## Slide 31: Tangent Bug

## Slide 32: Tangent Bug
full details
  Principles of Robot Motion: Theory, Algorithms, and Implementations
  http://www.library.yorku.ca/find/Record/2154237
nice animation
  http://www.cs.cmu.edu/~motionplanning/student_gallery/2006/st/hw2pub.htm