## Slide 1: Wireless LAN Security
CSE 6590

## Slide 2: Outline
Wired Equivalent Privacy (WEP)
  first security protocol defined in 802.11
Wi-Fi Protected Access (WPA)
  defined by Wi-Fi Alliance
WPA2
802.11i

## Slide 3: History
In the early 1980s, the IEEE began work on developing computer network architecture standards
  This work was called Project 802
In 1990, the IEEE formed a committee to develop a standard for WLANs (Wireless Local Area Networks)
  At that time WLANs operated at a speed of 1 to 2 million bits per second (Mbps)

## Slide 4: IEEE 802.11 WLAN Standard
In 1997, the IEEE approved the IEEE 802.11 WLAN standard
Revisions
  IEEE 802.11a
  IEEE 802.11b
  IEEE 802.11g
  IEEE 802.11n

## Slide 5: Controlling Access to a WLAN
Access is controlled by limiting a device’s access to the access point (AP)
Only devices that are authorized can connect to the AP
  One way: Media Access Control (MAC) address filtering
  CCSF uses this technique (unfortunately)
  See www.ccsf.edu/wifi

## Slide 6: Controlling Access

## Slide 7: MAC Address Filtering

## Slide 8: MAC Address Filtering
Usually implemented by permitting instead of preventing
CCSF does this
  www.ccsf.edu/wifi

## Slide 9: MAC Address Filtering Weaknesses
MAC addresses are transmitted in the clear
  An attacker can just sniff for MACs
Managing a large number of MAC addresses is difficult
MAC address filtering does not provide a means to temporarily allow a guest user to access the network
  Other than manually entering the user’s MAC address into the access point

## Slide 10: Wired Equivalent Privacy (WEP)
Designed to ensure that only authorized parties can view transmitted wireless information
Uses encryption to protect traffic
WEP was designed to be:
  Efficient and reasonably strong
10
Notes: 10

## Slide 11: WEP Keys
WEP secret keys can be 64 or 128 bits long
The AP and devices can hold up to four shared secret keys
  One of which must be designated as the default key

## Slide 13: WEP Encryption Process

## Slide 14: Cyclic Redundancy Check (CRC)
One of the most common and powerful error-detecting codes.
Given k bits of data,
generate a sequence F of j bits (FCS)
using a predetermined divisor P of (j+1) bits
Transmit a frame of k+j bits (data + FCS) which will be exactly divisible by divisor P
Receiver divides frame by divisor P
  If no remainder, assume no error
Notes: One of the most common, and one of the most powerful, error-detecting codes is the cyclic redundancy check (CRC), which can be described as follows. Given a k-bit block of bits, or message, the transmitter generates an (n – k)-bit sequence, known as a frame check sequence (FCS), such that the resulting frame, consisting of n bits, is exactly divisible by some predetermined number. The receiver then divides the incoming frame by that number and, if there is no remainder, assumes there was no error. Can state this procedure in three equivalent ways: modulo 2 arithmetic, polynomials, and digital logic, as detailed in Stallings DCC9e chapter 6.3. Comes down to working out what remainder exists when divide data by desired number, and using that as the FCS value appended to the data to form the block.

## Slide 16: WEP Encryption Process (2)
When a node has a packet to send, it first generates CRC for this packet as an integrity check value (ICV).
Generates an IV; concatenates it with the secret key; applies RC4 to create RC4 key stream.
Performs XOR operation on the above two streams, byte by byte, to produce ciphertext.
Appends the IV to the ciphertext and transmits to the receiver.

## Slide 17: WEP Encryption Process (3)

## Slide 18: Transmitting with WEP

## Slide 19: Analysis of WEP Encryption
IV is 24-bit long  224 choices.
The probability of choosing the same IV value is more than 99% after only 1200 frames.
Only a few seconds elapse with 11Mbps and 1KByte frame size.
IV values are sent in plain text  attackers can detect a duplicate value and re-use past keys.

## Slide 20: Breaking 802.11 WEP encryption
Security hole:
24-bit IV, one IV per frame, -> IV’s eventually reused
IV transmitted in plaintext -> IV reuse detected
Attack:
  Trudy causes Alice to encrypt known plaintext d1 d2 d3 d4 …
  Trudy sees: ci = di XOR kiIV
  Trudy knows ci di, so can compute kiIV
  Trudy knows encrypting key sequence k1IV k2IV k3IV …
  Next time IV is used, Trudy can decrypt!

## Slide 21: Device Authentication
Before a computer can connect to a WLAN, it must be authenticated
Types of authentication in 802.11
  Open system authentication
    Lets everyone in
  Shared key authentication
    Only lets computers in if they know the shared key

## Slide 24: WEP Summary
Authentication is first carried out via
  open system authentication, or
  shared key authentication
  Data packets are then encrypted using the WEP encryption process described above. Each packet requires a new IV.

## Slide 25: WEP Weaknesses
Static WEP keys (no periodic updates)
High frequency of repeating the same IV
  IVs are only 24-bit long
  Packets can be replayed to force the access point to pump out IVs.
CRC is weak in integrity check.
  An attacker can flip a bit in the encrypted data and then change the CRC as well.
Authentication is too simple.

## Slide 26: WPA

## Slide 27: WPA History
Wireless Ethernet Compatibility Alliance (WECA)
  A consortium of wireless equipment manufacturers and software providers
WECA goals:
  To encourage wireless manufacturers to use the IEEE 802.11 technologies
  To promote and market these technologies
  To test and certify that wireless products adhere to the IEEE 802.11 standards to ensure product interoperability

## Slide 28: WPA History (2)
In 2002, the WECA organization changed its name to Wi-Fi (Wireless Fidelity) Alliance
In October 2003 the Wi-Fi Alliance introduced Wi-Fi Protected Access (WPA)
  WPA had the design goal to protect both present and future wireless devices, addresses both wireless authentication and encryption
PSK or 802.11X addresses authentication and TKIP addresses encryption

## Slide 29: WPA: Improving WEP Encryption
Key size increased to 128 bits
Larger IVs: 48-bit long
Changing security keys through Temporary Key Integrity Protocol (TKIP)
  Encryption keys are changed (based on a master key) after a certain number of packets have been sent.
  An IV is mixed with data (not concatenate).
Ciphering scheme is the same as WEP
  compatible with old wireless LAN cards

## Slide 30: WPA: Improving Integrity Check
WPA uses a new message integrity check scheme called Michael, replacing the CRC function in WEP.
A frame counter is added to Michael to avoid replay or forgery attack.
Note: Ciphering scheme is the same as WEP.
  Compatible with old WLAN cards

## Slide 32: WPA Authentication
Two options:
PSK (inexpensive, home/personal networking)
802.1X (expensive, enterprise networking)

## Slide 33: WPA Personal Security
Pre-shared key (PSK) authentication
  Uses a passphrase to generate the encryption key
Key must be entered into both the access point and all wireless devices
  Prior to the devices communicating with the AP
The PSK is not used for encryption
  Instead, it serves as the starting point (seed) for mathematically generating the encryption keys
Results in a pair-wise master key (PMK)
Followed by a 4-way handshake to handle key management and distribution, which uses the PMK to generate a pair-wise transient key (PTK).

## Slide 34: WPA Personal Security (2)

## Slide 35: Pre-Shared Key Weakness
A PSK is a 64-bit hexadecimal number
  Usually generated from a passphrase
    Consisting of letters, digits, punctuation, etc. that is between 8 and 63 characters in length
If the passphrase is a common word, it can be found with a dictionary attack

## Slide 36: PSK Key Management Weaknesses
People may send the key by e-mail or another insecure method
Changing the PSK key is difficult
  Must type new key on every wireless device and on all access points
  In order to allow a guest user to have access to a PSK WLAN, the key must be given to that guest

## Slide 37: WPA Authentication via 802.11X
Three components:
  Remote authentication dial-in user service (RADIUS)
  authenticator (access point)
  supplicant (client)
Uses EAP authentication framework
  EAP-PSK, EAP-TLS, EAP-TTLS, EAP-MD5
Results in a pair-wise master key (PMK)
Followed by a 4-way handshake to handle key management and distribution, which uses the PMK to generate a pair-wise transient key (PTK).

## Slide 38: EAP-TLS

## Slide 39: EAP-TLS
AS verifies client’s digital signature using client’s public key got from client’s certificate Certclient
Get random number p by decrypting with its private key
Client calculates H(c,s,p), compares it with the value sent by As

## Slide 40: 4-way Handshake

## Slide 41: Key Hierarchy

## Slide 43: WPA2

## Slide 44: WPA2 Personal Security
Wi-Fi Protected Access 2 (WPA2)
  Introduced by the Wi-Fi Alliance in September 2004
  The second generation of WPA security
  Still uses PSK (Pre-Shared Key) authentication
  But instead of TKIP encryption it uses a stronger data encryption method called AES-CCMP
AES: Advanced Encryption Standard
CCMP: Counter Mode with Cipher Block Chaining Message Authentication Code Protocol

## Slide 45: WPA2 Personal Security (2)
PSK Authentication
  Intended for personal and small office home office users who do not have advanced server capabilities
  PSK keys are automatically changed and authenticated between devices after a specified period of time known as the rekey interval

## Slide 46: WPA2 Personal Security (3)
AES-CCMP Encryption
  Encryption under the WPA2 personal security model is accomplished by AES-CCMP
  This encryption is so complex that it requires special hardware to be added to the access points to perform it

## Slide 47: WPA and WPA2 Compared

## Slide 48: WPA2 Enterprise Security
The most secure method
Authentication uses IEEE 802.1x
Encryption is AES-CCMP

## Slide 49: Wireless Security Models

## Slide 50: 802.11i
A superset of all WLAN security mechanisms including WEP, WPA and WPA2.
PSK (personal) or 802.1X (enterprise) is used for authentication and key management.

## Slide 51: Reference
Section 6.3.1, Wireless Mesh Networks, by I. F. Akyildiz and X. Wang