## Slide 1: Scripts

## Slide 2: MATLAB Scripts
a script is text file containing a sequence of MATLAB commands
  each command usually occurs on a separate line of the file
MATLAB can run the commands in a script by reading the file and interpreting the text as MATLAB commands
  commands are run in order that they appear in the script file

## Slide 3: MATLAB Scripts
the filename of a MATLAB script always has the following form:
yourScriptName.m
where yourScriptName must be a valid MATLAB variable name
  i.e., must begin with a letter and may only contain letters and spaces and underscores
    no spaces or symbols!

## Slide 4: MATLAB scripts
scripts are useful for keeping a permanent record of a sequence of commands
typically, you will want to output the result of the script
  e.g., as a plot of some kind
  or as a message of some kind
also, you may want to save the results of the computations that the script has performed

## Slide 5: Text output
a MATLAB string is a row vector of characters
any text enclosed by single quotes is considered a MATLAB string
s = 'Any characters'
the string is actually a vector that contains the numeric codes for the characters (codes 0 to 127 are ASCII)
the length of S is the number of characters
a quotation within the string is indicated by two quotation marks

## Slide 6: Text output
the command disp will display a MATLAB string to the screen without displaying the name of the variable
>> s = 'Any characters'
s =
Any characters
>> disp(s)
Any characters

## Slide 7: Formatted output
it is often very useful to generate strings programmatically
  display output more elaborate than just a variable value
  display a table of values
  export data to a non-native MATLAB format
  generate the string for a MATLAB command
the function sprintf is used to generate formatted strings
  use doc sprintf to get help for sprintf
  help sprintf is less useful

## Slide 8: Formatted output
the syntax of the sprintf command is:
str = sprintf(formatSpec, A1, ..., An)
formatSpec is a formatting string with a large number of options
  probably inherited from the C programming language (or C's predecessor languages)
A1, ..., An are the arrays containing the information to format

## Slide 9: Formatted output
the formatting string describes how MATLAB should convert the information stored in the arrays into text
the formatting string can include:
  text
  escape characters
  zero or more percent signs each followed by:
    optional operator characters, and a conversion character

## Slide 10: Formatted output
examples using only plain text and escape characters
  see textbook or doc sprintf for a table of escape characters
>> sprintf('hi')
>> sprintf('''hi''')
>> sprintf('hi\tbye')
>> sprintf('hi\nbye')
>> sprintf('50%%')

## Slide 11: Formatted output
usually you will need to include a conversion character and an array containing data
  the conversion character tells MATLAB what conversion it should use when converting the data in the array to text
  most commonly used conversions are:
  %d base 10 integer
  %i base 10 integer
  %f fixed-point floating-point
  %e exponential notation
  %s string

## Slide 12: Formatted output
examples using simple conversions
>> n = 10;
>> sprintf('There are %d items', n)
>> degc = 100;
>> degf = (9 / 5) * degc + 32;
>> sprintf('%f deg C = %f deg F', degc, degf)
>> sprintf('%e deg C = %e deg F', degc, degf)
>> name = 'Jessica';
>> sprintf('Her name was %s', name)

## Slide 13: Formatted output
for floating-point conversions, you can specify the number of digits after the decimal place
  called the precision
  default value is 6
>> degc = 100;
>> degf = (9 / 5) * degc + 32;
>> sprintf('%.2f deg C = %.2f deg F', degc, degf)
>> sprintf('%.1e deg C = %.1e deg F', degc, degf)
>> sprintf('%.0f deg C = %.15f deg F', degc, degf)

## Slide 14: Formatted output
for all conversions, you can specify the minimum number of characters to output
>> n = 10;
>> sprintf('There are %5d items', n)
>> degc = 100;
>> degf = (9 / 5) * degc + 32;
>> sprintf('%8.1f deg C = %8.1f deg F', degc, degf)
>> name = 'Jessica';
>> sprintf('Her name was %15s', name)

## Slide 15: Formatted output
there are many other options in sprintf
  see doc sprintf for details
  experiment the options

## Slide 16: Formatted output
when using sprintf with an array, the formatting string is recycled columnwise through the elements of the array
>> A = [1 2 3 4; 5 6 7 8];
>> s = sprintf('%d %d\n', A)
s =
1 5
2 6
3 7
4 8

## Slide 17: Formatted output
when using sprintf with an array, the formatting string is recycled columnwise through the elements of the array
>> A = [1 2 3 4; 5 6 7 8; 9 10 11 12];
>> s = sprintf('%d %d\n', A)
s =
1 5
9 2
6 10
3 7
11 4
8 12

## Slide 18: Formatted output
when using sprintf with an array, the formatting string is recycled columnwise through the elements of the array
>> A = [1 2 3 4; 5 6 7 8; 9 10 11 12];
>> >> s = sprintf('%d %d %f %f\n', A)
s =
1 5 9.000000 2.000000
6 10 3.000000 7.000000
11 4 8.000000 12.000000

## Slide 19: Saving results to a file
you can save some or all of the variables in your workspace to a file that MATLAB can reload
the command
>> save
saves all of the workspace variables to a file named matlab.mat in the current working folder
the file is not human readable; it is saved as a MATLAB readable binary format

## Slide 20: Saving results to a file
the commands
>> save('myfile.mat')
>> save myfile.mat
saves all of the workspace variables to a file named myfile.mat in the current working folder

## Slide 21: Saving results to a file
the commands
>> save('myfile.mat', 'degc', 'degf', 'name')
>> save myfile.mat degc degf name
saves only the specified workspace variables to a file named myfile.mat in the current working folder

## Slide 22: Saving results to a file
the commands
>> save('myfile.mat', 'degc', 'degf', 'name')
>> save myfile.mat degc degf name
saves only the specified workspace variables to a file named myfile.mat in the current working folder

## Slide 23: Saving results to a file
if you want a human readable file specify the option '-ascii' and possibly '-double'
>> save('myfile.mat', 'degc', 'degf', 'name', '-ascii')
>> save myfile.mat degc degf name -ascii
this has severe limitations; I don't recommend using the '-ascii' option unless you are sure you know what you are doing

## Slide 24: Loading variables from a file
you can load a binary .mat file using the load command
  you get back the saved variables with their original names
>> load('myfile.mat')
>> load myfile.mat

## Slide 25: Loading variables from a file
load will also load a plain text file if it contains a rectangular table of numbers with an equal number of elements in each row
  for example, suppose you have a file mydata.dat that contains the following:
0.5377 -1.3077 -1.3499
1.8339 -0.4336 3.0349
-2.2588 0.3426 0.7254
0.8622 3.5784 -0.0631
0.3188 2.7694 0.7147

## Slide 26: Loading variables from a file
the command:
>> x = load('mydata.dat')
will load the contents of the file into the variable x