## Slide 1: CSE4421/5324: Introduction to Robotics

## Slide 2: Contact Information
Burton Ma Lassonde 2046 burton@cse.yorku.ca
EECS4421/5324 lectures Monday, Wednesday, Friday 2:30-3:30PM (CB 122) labs Thursday 11:30-1:30, Prism 1004 www.eecs.yorku.ca/course/4421 (web site not complete yet)

## Slide 3: General Course Information
introduces the basic concepts of robotic manipulators and autonomous systems. After a review of some fundamental mathematics the course examines the mechanics and dynamics of robot arms, mobile robots, their sensors and algorithms for controlling them.
one robotic arm (hopefully)
everything in Matlab
other references
  see course web page

## Slide 4: Labs
six 2-hour labs
  Thursday 11:30-1:30 in Prism LAS1004
  different lab sections alternate between weeks
    except possibly for Lab 01
  first part of Lab 01 already posted and must be completed prior to lab

## Slide 5: Assessment
labs/assignments 6 x 5%
midterm, 30%
exam, 40%

## Slide 6: Day 01
Introduction to manipulator kinematics

## Slide 7: Robotic Manipulators
a robotic manipulator is a kinematic chain
  i.e. an assembly of pairs of rigid bodies that can move respect to one another via a mechanical constraint
the rigid bodies are called links
the mechanical constraints are called joints

## Slide 8: A150 Robotic Arm
link 3
link 2

## Slide 9: Joints
most manipulator joints are one of two types
revolute (or rotary)
  like a hinge
  allows relative rotation about a fixed axis between two links
    axis of rotation is the z axis by convention
prismatic (or linear)
  like a piston
  allows relative translation along a fixed axis between two links
    axis of translation is the z axis by convention
our convention: joint i connects link i – 1 to link i
  when joint i is actuated, link i moves

## Slide 10: Joint Variables
revolute and prismatic joints are one degree of freedom (DOF) joints; thus, they can be described using a single numeric value called a joint variable
qi : joint variable for joint i
revolute
  qi = qi : angle of rotation of link i relative to link i – 1
prismatic
  qi = di : displacement of link i relative to link i – 1

## Slide 11: Revolute Joint Variable
revolute
  qi = qi : angle of rotation of link i relative to link i – 1
link i – 1
link i
qi

## Slide 12: Prismatic Joint Variable
prismatic
  qi = di : displacement of link i relative to link i – 1
link i – 1
link i
di

## Slide 13: Common Manipulator Arrangments
most industrial manipulators have six or fewer joints
  the first three joints are the arm
  the remaining joints are the wrist
it is common to describe such manipulators using the joints of the arm
  R: revolute joint
  P: prismatic joint

## Slide 14: Articulated Manipulator
RRR (first three joints are all revolute)
joint axes
  z0 : waist
  z1 : shoulder (perpendicular to z0)
  z2 : elbow (parallel to z1)
z0
z1
z2
waist
shoulder
elbow
forearm
q1
q2
q3

## Slide 15: Spherical Manipulator
RRP
Stanford arm
  http://infolab.stanford.edu/pub/voy/museum/pictures/display/robots/IMG_2404ArmFrontPeekingOut.JPG
z0
z1
z2
waist
shoulder
q1
q2
d3

## Slide 16: SCARA Manipulator
RRP
Selective Compliant Articulated Robot for Assembly
  http://www.robots.epson.com/products/g-series.htm
z0
z1
z2
q1
q2
d3

## Slide 17: Forward Kinematics
given the joint variables and dimensions of the links what is the position and orientation of the end effector?
q2
q1
a1
a2

## Slide 18: Forward Kinematics
choose the base coordinate frame of the robot
  we want (x, y) to be expressed in this frame
q2
q1
a1
a2
(x, y) ?
x0
y0

## Slide 19: Forward Kinematics
notice that link 1 moves in a circle centered on the base frame origin
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )

## Slide 20: Forward Kinematics
choose a coordinate frame with origin located on joint 2 with the same orientation as the base frame
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1

## Slide 21: Forward Kinematics
notice that link 2 moves in a circle centered on frame 1
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )

## Slide 22: Forward Kinematics
because the base frame and frame 1 have the same orientation, we can sum the coordinates to find the position of the end effector in the base frame
q2
q1
a1
a2
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )
(a1 cos q1 + a2 cos (q1 + q2),
a1 sin q1 + a2 sin (q1 + q2) )

## Slide 23: Forward Kinematics
we also want the orientation of frame 2 with respect to the base frame
  x2 and y2 expressed in terms of x0 and y0
q2
q1
a1
a2
x0
y0
q1
x2
y2

## Slide 24: Forward Kinematics
without proof I claim:
q2
q1
a1
a2
x0
y0
q1
x2 = (cos (q1 + q2),
sin (q1 + q2) )
y2 = (-sin (q1 + q2),
cos (q1 + q2) )
x2
y2

## Slide 25: Forward Kinematics
find , , and expressed in frame
d1
x0
y0
q2
x2
y2
x1
y1
(x, y) ?

## Slide 26: Forward Kinematics
find , , and expressed in frame
x0
y0
d1
q2
x2
y2
x1
y1
(x, y) ?

## Slide 27: Inverse Kinematics
given the position (and possibly the orientation) of the end effector, and the dimensions of the links, what are the joint variables?
q2 ?
q1 ?
a1
a2
x0
y0
x2
y2
(x, y)

## Slide 28: Inverse Kinematics
harder than forward kinematics because there is often more than one possible solution
a1
a2
x0
y0
(x, y)

## Slide 29: Inverse Kinematics
law of cosines
q2 ?
a1
a2
x0
y0
(x, y)
b

## Slide 30: Inverse Kinematics
and we have the trigonometric identity
therefore,
We could take the inverse cosine, but this gives only one of the two solutions.

## Slide 31: Inverse Kinematics
to obtain
Instead, use the two trigonometric identities:
which yields both solutions for q2 . In many programming languages you would use the
four quadrant inverse tangent function atan2
c2 = (x*x + y*y – a1*a1 – a2*a2) / (2*a1*a2);
s2 = sqrt(1 – c2*c2);
theta21 = atan2(s2, c2);
theta22 = atan2(-s2, c2);

## Slide 32: Inverse Kinematics
Exercise for the student: show that