## Slide 1: Day 05
Forward Kinematics

## Slide 2: Links and Joints
n joints, n + 1 links
link 0 is fixed (the base)
joint i connects link i – 1 to link i
  link i moves when joint i is actuated
joint 1
joint 2
joint 3
joint 4
joint n-1
joint n
link 0
link 1
link 2
link 3
link n-1
link n
.................

## Slide 3: Forward Kinematics
given the joint variables and dimensions of the links what is the position and orientation of the end effector?
q2
q1
a1
a2
x0
y0
p0 ?

## Slide 4: Forward Kinematics
because the base frame and frame 1 have the same orientation, we can sum the coordinates to find the position of the end effector in the base frame
q2
q1
a1
a2
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )
(a1 cos q1 + a2 cos (q1 + q2),
a1 sin q1 + a2 sin (q1 + q2) )

## Slide 5: Forward Kinematics
from Day 02
q2
q1
a1
a2
x0
y0
q1
x2 = (cos (q1 + q2),
sin (q1 + q2) )
y2 = (-sin (q1 + q2),
cos (q1 + q2) )
x2
y2
p0 = (a1 cos q1 + a2 cos (q1 + q2),
a1 sin q1 + a2 sin (q1 + q2) )

## Slide 6: Frames
q2
q1
a1
a2
x0
y0
x1
y1
x2
y2

## Slide 7: Forward Kinematics
using transformation matrices

## Slide 8: Links and Joints
n joints, n + 1 links
link 0 is fixed (the base)
joint i connects link i – 1 to link i
  link i moves when joint i is actuated
joint 1
joint 2
joint 3
joint 4
joint n-1
joint n
link 0
link 1
link 2
link 3
link n-1
link n
.................

## Slide 9: Forward Kinematics
attach a frame {i} to link i
  all points on link i are constant when expressed in {i}
  if joint i is actuated then frame {i} moves relative to frame {i - 1}
    motion is described by the rigid transformation
    the state of joint i is a function of its joint variable qi (i.e., is a function of qi)
this makes it easy to find the last frame with respect to the base frame

## Slide 10: Forward Kinematics
more generally
the forward kinematics problem has been reduced to matrix multiplication

## Slide 11: Forward Kinematics
Denavit J and Hartenberg RS, “A kinematic notation for lower-pair mechanisms based on matrices.” Trans ASME J. Appl. Mech, 23:215–221, 1955
  described a convention for standardizing the attachment of frames on links of a serial linkage
common convention for attaching reference frames on links of a serial manipulator and computing the transformations between frames

## Slide 12: Denavit-Hartenberg

## Slide 13: Denavit-Hartenberg

## Slide 14: Denavit-Hartenberg
notice the form of the rotation component
  this does not look like it can represent arbitrary rotations
can the DH convention actually describe every physically possible link configuration?

## Slide 15: Denavit-Hartenberg
yes, but we must choose the orientation and position of the frames in a certain way
  (DH1)
  (DH2)
claim: if DH1 and DH2 are true then there exists unique numbers

## Slide 16: Denavit-Hartenberg
proof: on blackboard in class