## Slide 1: Unscented Kalman Filter

## Slide 2: Linearization via Unscented Transform
EKF
UKF

## Slide 3: Unscented Transform
intuition: it should be easier to approximate a given distribution than it is to approximate an arbitrary non-linear function
  it is easy to transform a point through a non-linear function
  use a set of points that capture the mean and covariance of the distribution, transform the points through the non-linear function, then compute the (weighted) mean and covariance of the transformed points

## Slide 4: Empirical transformation of a Gaussian random variable
% generate 500,000 samples from N(0, 1)
x = randn(1, 500000);
% draw the histogram of x
xc = -5:0.2:5;
nx = hist(x, xc);
bar(xc, nx, 1);
% transform each sample by f(x)
y = nthroot(x – 1, 3);
% draw the histogram of y
xc = -2:0.1:2;
ny = hist(y, xc);
bar(xc, ny, 1);

## Slide 5: Empirical transformation of a Gaussian random variable
-transform 500,000 random
samples through a non-linear
function

## Slide 6: Unscented Transform
-transform 3 carefully chosen
samples through a non-linear
function
-samples are called sigma points

## Slide 7: UKF Sigma-Point Estimate (2)
EKF
UKF

## Slide 8: UKF Sigma-Point Estimate (3)
EKF
UKF

## Slide 9: UKF Sigma-Point Estimate (4)

## Slide 10: Unscented Transform
for an n-dimensional Gaussian with mean μ and covariance Σ , the unscented transform uses 2n+1 sigma points (and associated weights)
Sigma points Weights

## Slide 11: Unscented Transform
choose κ ≥ 0 to guarantee a “reasonable” covariance matrix
  value is not critical, so choose κ = 0 by default
choose 0 ≤ α ≤ 1
  controls the spread of the sigma point distribution; should be small when nonlinearities are strong
choose β ≥ 0
  β = 2 is optimal if distribution is Gaussian

## Slide 12: Unscented Transform
Pass sigma points through nonlinear function
Recover mean and covariance

## Slide 13
UKF_localization ( mt-1, St-1, ut, zt, m):
Prediction:
Motion noise
Measurement noise
Augmented state mean
Augmented covariance
Sigma points
Prediction of sigma points
Predicted mean
Predicted covariance

## Slide 14
UKF_localization ( mt-1, St-1, ut, zt, m):
Correction:
Measurement sigma points
Predicted measurement mean
Pred. measurement covariance
Cross-covariance
Kalman gain
Updated mean
Updated covariance

## Slide 15: UKF Prediction Step

## Slide 16: UKF Observation Prediction Step

## Slide 17: UKF Correction Step

## Slide 18: Estimation Sequence
EKF PF UKF

## Slide 19: Estimation Sequence
EKF UKF

## Slide 20: Prediction Quality
EKF UKF
velocity_motion_model

## Slide 21: UKF Summary
Highly efficient: Same complexity as EKF, with a constant factor slower in typical practical applications
Better linearization than EKF: Accurate in first two terms of Taylor expansion (EKF only first term)
Derivative-free: No Jacobians needed
Still not optimal!