## Slide 1: Opportunistic Mobile Social Networks
Farzana Yasmeen
Dept. of Computer Science and Engineering
York University, Toronto, Canada
Date: Nov. 2, 2017

## Slide 2: Overview
Introduction to Opportunistic/Delay-Tolerant Networks (DTN)
Problem domain: Routing in Opportunistic Networks
Overlay – Social Properties
Highlights of the Solution Space
SimBet Routing

## Slide 3: All People Seem to Need Data Processing
http://www.tech-faq.com/osi-model.html
TCP/IP Model
Application Layer
Data Flow Layer

## Slide 4: Some Communication Networks
Wireless Networks
Sensor Networks
Satellite Networks
Mobile Ad hoc networks (MANETs)
Voice Over IP (VoIP)
Internet of Things (IoT)
Delay-tolerant Networks
Online Social Networks

## Slide 5: MANET Routing Protocols

## Slide 6: Delay-Tolerant Networks

## Slide 7: Intermittent Connectivity
    Intermittent connectivity:
    mobility, geography, infrastructure, energy conservation
    - high error rates, long delays in transmission, low throughput
A
B
E
D
F
C

## Slide 8: A virtually connected network
Store-Carry-Forward:
  Hop-by-hop instead of end-to-end
  Persistent storage
  Custody transfer mechanism
  Rely on opportunity
A
B
E
D
F
C
S
D
M
detect next hop
forward
detect next hop
wait for link to come up
forward
i
M
i
detect next hop
forward
M

## Slide 9: DTN – Interplanetary Networks
The world's national space agencies are constructing a DTN called the Solar System Internetwork (http://public.ccsds.org/publications/archive/730x1g1.pdf)
that uses the ipn scheme name.
http://ipnsig.org/wp-content/uploads/2015/09/DTN_Tutorial_v3.2.pdf

## Slide 10: DTN – Vehicular Networks

## Slide 11: DTN – Rural Area Communication

## Slide 12: Combine across protocol stack

## Slide 13: DTN – Mobile Social Network (MSN)

## Slide 14: DTN vs MANET
Multihop ad hoc network
Delay-tolerant network
http://www.meshdynamics.com/military-mesh-networks.html
Store – Carry – Forward
M
M
A
B
C
t
link estb.
End-to-end delivery from A to C  1 min
Route search among multiple hops
Delivery from source to destination
frwrd msg to link
A
B
C
t
End-to-end delivery from A to C  1 hour
Route search among multiple hops
Delivery from source to destination
link estb.
frwrd msg to link
frwrd msg to link

## Slide 15: Disruption-Tolerant Networks
https://www.youtube.com/watch?v=nWtRTzXJvtI

## Slide 16: Overlay Approach

## Slide 17: DTN in Action

## Slide 18: Motivation
Motivation for Routing:
Motivation for DTN:
  Store-n-forward overlay hides lower-layer disparity from the application
  Longer delay is tolerable than no communication at all, as there is no infrastructure
Legacy applications: File Transfer, Email, Cached Web
Communication possible when devices are within communication range of each other
Physical proximity is important
Opportunistic contacts are called encounters
A
B
C
D
E
F
Sparse Wireless Network

## Slide 19: Routing Objectives: Improve the capacity of the Network
Minimize end-end delay for messages
Maximize network delivery ratio
t2
t7
t5
A, B meet
contact duration
inter-contact time
A
(sender)
t1
msg. generated at A
t3
Routing Decision to B
and check transmitter availability
t4
start transmit to B
t5
send last bit of msg. to B
t9
B receives msg.
can be very large in DTN
transmission delay = T.D.
encounter delay = E.D.
propagation delay = P.D.
queuing delay = Q.D.
Check receiver availability
B
C
(receiver)
t8
E.D.
T.D.
P.D.
Q.D.
A, B can be apart
B, C meet
C receives msg.

## Slide 20: DTN Metrics (1)
Average message delivery ratio: The message delivery ratio of a destination d is the ratio of the number of unique messages for d generated by its source(s) and successfully received by d to the total number of unique messages created. The average message delivery ratio is the average of the delivery ratios of all the destinations in the network.
Average end-to-end delay: The end-to-end delay of every message successfully received at every destination is recorded. Once the copy of a particular message is received at the final destination, subsequent copies are disregarded. The average over all the messages received is then computed.

## Slide 21: DTN Metrics (2)
Average buffer time: The buffer time for a message m is the interval between the time the message is saved in the buffer of a node to the time it is removed from the buffer of that node. Essentially, it is the time the message was queued in the node’s buffer. The average buffer time is the average taken over all messages stored at every node in the network.
Average buffer time significantly impacts a DTNs performance as:
(a) it is an indicator of how fast messages are being forwarded at nodes, and thus are propagating through the network, as longer buffer time leads to longer end-to-end delays; and
(b) the longer messages are stored in buffers the more buffer overflows will occur, leading to higher loss rates.

## Slide 22: DTN Metrics (3)
Average overhead ratio:
where H is the number of hops a message m and all copies of m traverse in the network before a copy is successfully delivered to the intended recipient, and hd is the number of hops the delivered message (or its copy) had traversed before reaching the final destination.
It represents the quantity of excessive relays required to deliver the message and quantifies the bandwidth and energy consumption of the routing protocol
Average number of contact opportunities per hour: We define a ‘contact opportunity’ as two nodes coming within the wireless transmission range of each other, presenting an opportunity to transfer messages.

## Slide 23: DTN Routing Protocols
Epidemic Routing
[paper] http://issg.cs.duke.edu/epidemic/epidemic.pdf
[title] Epidemic Routing for Partially-Connected Ad Hoc Networks
PRoPHET
[paper] http://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.59.6027&rep=rep1&type=pdf
[title] Probabilistic routing in intermittently connected networks
Spray-n-Wait
[paper] https://dl.acm.org/citation.cfm?id=1080143
[title] Spray and wait: An efficient routing scheme for intermittently connected mobile networks.

## Slide 24: Epidemic Protocol – Random forwarding
Forward to any encountered node

## Slide 25: Epidemic Routing
Message Duplication
Transmission overhead
M
S
D
M
M
M
M
M
M
M
M
M

## Slide 26: Summary Vector Exchange

## Slide 27: PRoPHET Protocol– Probabilistic forwarding
probabilistic metric -> delivery predictability : 0 <= P(a,b) <= 1
The delivery predictability metric, P(a,b) has three properties, based on which it is (re)calculated:
update,
aging, and
transitivity.

## Slide 28: PRoPHET Routing
S
D
B
C
E
G
H
I
A
P(A,B), P(A,D) P(A,F), P(A,H)
P(B,A), P(B,E) P(B,G)
P(C,G), P(C,D)
P(E,B), P(E,D)
P(G,B), P(G,C)
P(H,A), P(H,S)
F
P(F,A), P(F,D)
P(I,D)
P(D,A), P(D,C) P(D,F), P(D,I)
P(S,D), P(S,H)
M
P(S,D), >P(A,D)
P(F,D), >P(A,D)
M
M
M
Transmission overhead

## Slide 29: Spray-n-Wait
Spray and Wait (SnW) protocol is an n-copy routing protocol. This routing algorithm consists of two phases:
Spray phase: for every message M originating at a source node, K copies of the message are initially spread (forwarded by the source and possibly other nodes receiving a copy) to “K” distinct relays (i.e. intermediate nodes).
Wait phase: if the destination is not found in the spraying phase, each of the K nodes carrying a message copy performs direct transmission (i.e. will forward the message only to its destination).

## Slide 30: Simulations (with contention, waypoint model)
Simulated schemes
  Epidemic routing
  Randomized flooding (p = 0.03)
  Utility-based flooding (Uth = 0.02)
  Constrained utility-based flooding
  Source Spray and Wait (L = 10)
  Optimal Spray and Wait (L = 10)
  Seek and Focus
  Oracle-based optimal algorithm
Same collision avoidance MAC protocol and utility function as before

## Slide 31: Scenario A (low traffic)
Spray and Wait
  Low delay (twice that of the optimal), small # of transmissions (even less than seek and focus)
  achieves a lower delay than utility-based schemes
500x500, M = 50 nodes, K = 20

## Slide 32: Scenario B (high traffic)
Spray and Wait achieves up to an order of magnitude reduction in number of transmission compared to flooding and utility-based schemes
and a delivery delay lower than all other schemes
500x500, M = 50, K = 20 (6% coverage), 40 (25% coverage)

## Slide 33: Opportunistic Mobile Networks
inherent (random) movement of nodes
flooding, multi-copy
probabilistic contacts
controlled movement of auxiliary nodes
deterministic contacts
Optimal MF design

## Slide 34: Opportunistic Mobile Social Networks (OMNS)
Characteristics of mobile nodes in opportunistic MSNs are:
Opportunistic contacts
Mobility
Social Features
Social Relationships A social graph G=(V,E,W)

## Slide 35: OMNS Routing

## Slide 36: SimBet – It’s a small world
[paper] https://dl.acm.org/citation.cfm?id=1288113
[title] Social Network Analysis for Routing in Disconnected Delay-Tolerant MANETs

## Slide 37: Centrality
Centrality in graph theory and network analysis is a quantification of the relative importance of a vertex within the graph (e.g., how important a person is within a social network).
The centrality of a node in a network is a measure of the structural importance of the node.
A central node, typically, has a stronger capability of connecting other network members.
There are several ways to measure centrality. The three most widely used centrality measures are Freeman’s degree, closeness, and betweenness measures

## Slide 38: Degree centrality
A node with high degree centrality maintains contacts with numerous other network nodes. Such nodes can be seen as popular nodes with large numbers of links to others.
As such, a central node occupies a structural position (network location) that may act as a conduit for information exchange.

## Slide 39: Closeness Centrality

## Slide 40: Betweenness Centrality

## Slide 41: Socio vs Ego Networks

## Slide 42: Betweenness Calculation
The betweenness of the ego node is the sum of the reciprocals of the entries of
A2 [1 − A]i,j

## Slide 43: Similarity Calculation

## Slide 44: SimBet Utility Metrics

## Slide 45: SimBet Algorithm

## Slide 46: Betweenness Distribution

## Slide 47: Betweenness Distribution

## Slide 48: Friendship network Eagle and Pentland

## Slide 49: Simulation Results: Each node sending a message to each other node in the network

## Slide 50: Percentage of message delivered between a subset of nodes increasing based on increased Betweenness

## Slide 51: Conclusions
These forwarding metrics may prove useful in other distributed systems where global topology information is unavailable, especially where the underlying networks exhibit small-world characteristics.

## Slide 52
Thank You