## Slide 1: Wireless LAN Security
CSE 6590

## Slide 2: Outline
Wired Equivalent Privacy (WEP)
  first security protocol defined in 802.11
Wi-Fi Protected Access (WPA)
  defined by Wi-Fi Alliance
WPA2
802.11i

## Slide 3: History
In the early 1980s, the IEEE began work on developing computer network architecture standards
  This work was called Project 802
In 1990, the IEEE formed a committee to develop a standard for WLANs (Wireless Local Area Networks)
  At that time WLANs operated at a speed of 1 to 2 million bits per second (Mbps)

## Slide 4: IEEE 802.11 WLAN Standard
In 1997, the IEEE approved the IEEE 802.11 WLAN standard
Revisions
  IEEE 802.11a
  IEEE 802.11b
  IEEE 802.11g
  IEEE 802.11n
  IEEE 802.11ac
  IEEE 802.11ad (WiGig)

## Slide 5: Controlling Access to a WLAN
Access is controlled by limiting a device’s access to the access point (AP)
Only devices that are authorized can connect to the AP
  One way: Media Access Control (MAC) address filtering
    Easily breakable!

## Slide 6: Controlling Access

## Slide 7: MAC Address Filtering

## Slide 8: MAC Address Filtering
Usually implemented by permitting instead of preventing
Some universities does this:
  YorkU does it for LAN users 

## Slide 9: MAC Address Filtering Weaknesses
MAC addresses are transmitted in the clear
  An attacker can just sniff for MACs
Managing a large number of MAC addresses is difficult
MAC address filtering does not provide a means to temporarily allow a guest user to access the network
  Other than manually entering the user’s MAC address into the access point

## Slide 10: Wired Equivalent Privacy (WEP)
Designed to ensure that only authorized parties can view transmitted wireless information
Uses encryption to protect traffic
WEP was designed to be:
  Efficient and reasonably strong
10
Notes: 10

## Slide 11: WEP Keys
WEP secret keys can be 64 or 128 bits long
The AP and devices can hold up to four shared secret keys
  One of which must be designated as the default key

## Slide 13: Device Authentication
Before a computer can connect to a WLAN, it must be authenticated
Types of authentication in 802.11
  Open system authentication
    Lets everyone in
  Shared key authentication
    Only lets computers in if they know the shared key

## Slide 16: WEP Encryption Process

## Slide 17: Transmitting with WEP

## Slide 18: Pre-Shared Key (PSK) Method
A 64-bit WEP key is a string of 10 hexadecimal + 24 bits Initial Vector (IV):
  That is 40 bits PSK key (10x4bits) + 24 bits IV
A 128-bit WEP key a string of 26 hexadecimal characters + 24 bits IV:
  That is 26x4 + 24 bits = 128

## Slide 19: WEP Weakness
24 bits of IV are sent in plaintext
  Recycled almost in 224 frames
    That is 4 reuse in every 5,000 packets
We can create large number of packets and thus compare two cipher text with the same IV and Key
Using packet injection we can achieve this goal:
  C1 xor C2 = (P1 xor K) xor (P2 xor K) = P1 xor P2
  Know P1/P2 and IV -> Key output

## Slide 20: WEP Frame
new IV for each frame
8-20
encrypted
data
ICV
IV
MAC payload
Key ID

## Slide 21: Breaking 802.11 WEP encryption
Security hole:
24-bit IV, one IV per frame, -> IV’s eventually reused
IV transmitted in plaintext -> IV reuse detected
Attack:
  Trudy causes Alice to encrypt known plaintext d1 d2 d3 d4 …
  Trudy sees: ci = di XOR kiIV
  Trudy knows ci di, so can compute kiIV
  Trudy knows encrypting key sequence k1IV k2IV k3IV …
  Next time IV is used, Trudy can decrypt!

## Slide 22: WEP Summary
Authentication is first carried out via
  open system authentication, or
  shared key authentication
  Data packets are then encrypted using the WEP encryption process described above. Each packet requires a new IV.

## Slide 23: WPA

## Slide 24: WPA: Improving WEP Encryption
Key size increased to 128 bits
Larger IVs: 48-bit long
Changing security keys through Temporary Key Integrity Protocol (TKIP)
  Encryption keys are changed (based on a master key) after a certain number of packets have been sent.
  An IV is mixed with data (not concatenate).

## Slide 26: WPA Authentication
Two options:
PSK (inexpensive, home/personal networking)
802.1X (expensive, enterprise networking)

## Slide 27: WPA Personal Security
Pre-shared key (PSK) authentication
  Uses a passphrase to generate the encryption key
Key must be entered into both the access point and all wireless devices
  Prior to the devices communicating with the AP
The PSK is not used for encryption
  Instead, it serves as the starting point (seed) for mathematically generating the encryption keys
Results in a pair-wise master key (PMK)
Followed by a 4-way handshake to handle key management and distribution, which uses the PMK to generate a pair-wise transient key (PTK).

## Slide 28: Pre-Shared Key Weakness
A PSK is a 64-bit hexadecimal number
  Usually generated from a passphrase
    Consisting of letters, digits, punctuation, etc. that is between 8 and 63 characters in length
If the passphrase is a common word, it can be found with a dictionary attack

## Slide 29: WPA Authentication via 802.1X
Three components:
  Remote authentication dial-in user service (RADIUS)
  authenticator (access point)
  supplicant (client)
Uses EAP authentication framework
  EAP-PSK, EAP-TLS, EAP-TTLS, EAP-MD5
Results in a pair-wise master key (PMK)
Followed by a 4-way handshake to handle key management and distribution, which uses the PMK to generate a pair-wise transient key (PTK).

## Slide 30: EAP-TLS

## Slide 31: WPA2

## Slide 32: WPA2 Personal Security
Wi-Fi Protected Access 2 (WPA2)
  Introduced by the Wi-Fi Alliance in September 2004
  The second generation of WPA security
  Still uses PSK (Pre-Shared Key) authentication
  But instead of TKIP encryption it uses a stronger data encryption method called AES-CCMP
AES: Advanced Encryption Standard
CCMP: Counter Mode with Cipher Block Chaining Message Authentication Code Protocol

## Slide 33: WPA2 Personal Security (2)
PSK Authentication
  Intended for personal and small office home office users who do not have advanced server capabilities
  PSK keys are automatically changed and authenticated between devices after a specified period of time known as the rekey interval

## Slide 34: WPA2 Personal Security (3)
AES-CCMP Encryption
  Encryption under the WPA2 personal security model is accomplished by AES-CCMP
  This encryption is so complex that it requires special hardware to be added to the access points to perform it

## Slide 35: WPA and WPA2 Compared

## Slide 36: WPA2 Enterprise Security
The most secure method
Authentication uses IEEE 802.1x
Encryption is AES-CCMP
  We can still crack it if it is PSK!

## Slide 37: 802.11i
A superset of all WLAN security mechanisms including WEP, WPA and WPA2.
PSK (personal) or 802.1X (enterprise) is used for authentication and key management.

## Slide 38: Reference
Section 6.3.1, Wireless Mesh Networks, by I. F. Akyildiz and X. Wang

## Slide 39: Demo Time (1)
Setup
  1. Let’s bring up the adapter
    ifconfig wlan0 up
  2. Start monitoring interface
    airmon-ng start wlan0
  3. Gather information on accesspoints:
    airodump-ng wlan0mon
  4. Find the accesspoint to attack
    airodump-ng –bssid AP_MAC –channel AP_CH –write demo wlan0mon
  5. Wait for a client to connect…
    Or deauth them:
      aireplay-ng -0 10 –a –c CLIENT ADAPTER

## Slide 40: Demo Time (2)
Crack Time
  aircrack-ng CAPFILE –w WORDLIST

## Slide 41: Appendix

## Slide 42: Cyclic Redundancy Check (CRC)
One of the most common and powerful error-detecting codes.
Given k bits of data,
generate a sequence F of j bits (FCS)
using a predetermined divisor P of (j+1) bits
Transmit a frame of k+j bits (data + FCS) which will be exactly divisible by divisor P
Receiver divides frame by divisor P
  If no remainder, assume no error
Notes: One of the most common, and one of the most powerful, error-detecting codes is the cyclic redundancy check (CRC), which can be described as follows. Given a k-bit block of bits, or message, the transmitter generates an (n – k)-bit sequence, known as a frame check sequence (FCS), such that the resulting frame, consisting of n bits, is exactly divisible by some predetermined number. The receiver then divides the incoming frame by that number and, if there is no remainder, assumes there was no error. Can state this procedure in three equivalent ways: modulo 2 arithmetic, polynomials, and digital logic, as detailed in Stallings DCC9e chapter 6.3. Comes down to working out what remainder exists when divide data by desired number, and using that as the FCS value appended to the data to form the block.

## Slide 44: WEP Encryption Process
When a node has a packet to send, it first generates CRC for this packet as an integrity check value (ICV).
Generates an IV; concatenates it with the secret key; applies RC4 to create RC4 key stream.
Performs XOR operation on the above two streams, byte by byte, to produce ciphertext.
Appends the IV to the ciphertext and transmits to the receiver.

## Slide 45: WEP Encryption Process (3)

## Slide 46: WPA History
Wireless Ethernet Compatibility Alliance (WECA)
  A consortium of wireless equipment manufacturers and software providers
WECA goals:
  To encourage wireless manufacturers to use the IEEE 802.11 technologies
  To promote and market these technologies
  To test and certify that wireless products adhere to the IEEE 802.11 standards to ensure product interoperability

## Slide 47: WPA History (2)
In 2002, the WECA organization changed its name to Wi-Fi (Wireless Fidelity) Alliance
In October 2003 the Wi-Fi Alliance introduced Wi-Fi Protected Access (WPA)
  WPA had the design goal to protect both present and future wireless devices, addresses both wireless authentication and encryption
PSK or 802.1X addresses authentication and TKIP addresses encryption

## Slide 48: PSK Key Management Weaknesses
People may send the key by e-mail or another insecure method
Changing the PSK key is difficult
  Must type new key on every wireless device and on all access points
  In order to allow a guest user to have access to a PSK WLAN, the key must be given to that guest

## Slide 49: EAP-TLS
AS verifies client’s digital signature using client’s public key got from client’s certificate Certclient
Get random number p by decrypting with its private key
Client calculates H(c,s,p), compares it with the value sent by As
Notes: EAP: extendable authentication protocol
TLS: transport layer security

## Slide 50: 4-way Handshake

## Slide 51: Key Hierarchy
Notes: key derivation function (KDF)
pseudorandom function family (PRF)
CCMP: TK = 128 bits
TKIP: TK = 256 bits

## Slide 52
Notes: RSN-IE (Robust Security Network Information Element): indicates the cipher algorithms used (CCMP, TKIP, WEP-104, WEP-40)

## Slide 53: Wireless Security Models