## Slide 1: Bug Algorithms

## Slide 2: Fundamental Problems
Chapter 2 of Dudek and Jenkin begins:
  "Before delving into the harsh realities of real robots...“
lists 5 fundamental problems
  path planning
  localization
  sensing or perception
  mapping
  simultaneous localization and planning

## Slide 3: A Point Robot
represents a mobile robot as a point in the plane*
the point P fully describes the state of the robot
  called pose or configuration
robot motion causes the state to change

## Slide 4: Free Space and Obstacles
the set of valid poses is called the free space Cfree of the robot
the invalid poses are obstacles
obstacle
obstacle
obstacle
obstacle
freespace
point
robot
obstacle

## Slide 5: Path Planning
is it possible for the robot to move to a goal configuration while remaining in Cfree ?
obstacle
obstacle
obstacle
obstacle
freespace
start
obstacle
goal

## Slide 6: Path Planning Using Bugs
bug algorithms assume:
  point robot
  known goal location
  finite number of bounded obstacles
  robot can perfectly sense its position at all times
  robot can compute the distance between two points
  robot can remember where it has been
  robot can perfectly sense its local environment
  robot can instantaneously change direction

## Slide 7: Bug Zero
assumes a perfect contact sensor
repeat
  head towards goal
  if goal is reached then stop
  if an obstacle is reached then follow the boundary until heading towards the goal is again possible

## Slide 8: Bug Zero
obstacle
obstacle
obstacle
obstacle
freespace
start
obstacle
goal
a right turning bug

## Slide 9: Bug Zero
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 10: Bug Zero
not guaranteed to reach the goal
obstacle
goal
start
gets stuck here because
as soon as it moves down
there is a path to the goal
that does not go through
the obstacle

## Slide 11: Bug One
assumes a perfect contact sensor
repeat:
  head toward goal T
  if goal is reached then stop
  if an obstacle is reached then
    remember the point of first contact H (the hit point)
    follow the boundary of the obstacle until returning to H and remember the point L (the leave point) closest to T from which the robot can depart directly towards T
      if no such point L exists then the goal is unreachable; stop
    move to L using the shortest boundary following path

## Slide 12: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 13: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
L

## Slide 14: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
L

## Slide 15: Bug One
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal

## Slide 16: Bug One

## Slide 17: Bug Two
Bug Two uses a line, called the m-line, from the start point to the goal
  sometimes called the direct path
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
m-line, or direct path

## Slide 18: Bug Two
assumes a perfect contact sensor
repeat:
  head toward goal T along the m-line
  if goal is reached then stop
  if an obstacle is reached then
    remember the point of first contact H (the hit point)
    follow the boundary of the obstacle until the m-line is crossed at a leave point closer to the goal than H
      if no such point L exists then the goal is unreachable; stop
    leave the obstacle and head toward T

## Slide 19: Bug Two
obstacle
obstacle
obstacle
obstacle
start
obstacle
goal
m-line, or direct path

## Slide 20: Bug Two

## Slide 21: Bug One versus Bug Two
Bug One uses exhaustive search
  it considers all leave points before leaving the obstacle
Bug Two uses greedy search
  it takes the first leave point that is closer to the goal

## Slide 22: Sensing the Environment
Bug1 and Bug2 use a perfect contact sensor
we might be able to achieve better performance if we equip the robot with a more powerful sensor
a range sensor measures the distance to an obstacle; e.g., laser range finder
  emits a laser beam into the environment and senses reflections from obstacles
  essentially unidirectional, but the beam can be rotated to obtain 360 degree coverage
  http://velodynelidar.com/lidar/lidar.aspx

## Slide 23: Tangent Bug
assumes a perfect 360 degree range finder with a finite range
  measures the distance r(x, q) to the first obstacle intersected by the ray from x with angle q
  has a maximum range beyond which all distance measurements are considered to be r = 
the robot looks for discontinuities in r(x, q)

## Slide 24: Tangent Bug
O1
O2
O3
O4
O5
O6

## Slide 25: Tangent Bug

## Slide 26: Tangent Bug
currently, bug thinks goal is reachable so it moves toward the goal
  called “motion to goal” mode
goal

## Slide 27: Tangent Bug
once the obstacle is sensed, the bug needs to decide how to navigate around the obstacle
move towards the sensed point Oi that minimizes the distance d(x, Oi) + d(Oi, qgoal) (called the heuristic distance)
goal
O1
O2

## Slide 28: Tangent Bug
the bug senses O1 and O2 so it moves towards O2 because
d(x, O2) + d(O2, qgoal) < d(x, O1) + d(O1, qgoal)
goal
O1
O2

## Slide 29: Tangent Bug
the bug senses O1 and O2 so it moves towards O2 because
d(x, O2) + d(O2, qgoal) < d(x, O1) + d(O1, qgoal)
goal
O1
O2

## Slide 30: Tangent Bug

## Slide 31: Tangent Bug

## Slide 32: Tangent Bug
heuristic distance as bug performs "motion to goal"

## Slide 33: Tangent Bug
problem with concave obstacles
  eventually the robot reaches a point where d(x, Oi) + d(Oi, qgoal) starts to increase
  once this happens, the robot switches to “boundary following” mode

## Slide 34: Tangent Bug
when the robot switches to "boundary following" mode it continuously updates two distances and the discontinuities in the range sensor measurements
    the shortest distance between the boundary which had been sensed since entering boundary following mode and the goal
    when the robot exits boundary following bode is reset to
    the distance between the goal and the closest point on the followed obstacle that is within line of sight of the robot
    the set of points in line of sight of the robot that cause discontinuities in the range finder measurements r(x, q)

## Slide 35: Tangent Bug
at the moment the robot enters "boundary following" mode

## Slide 36: Tangent Bug
in "boundary following" mode, the robot moves towards the point that is most consistent with the direction that the robot is currently moving in

## Slide 37: Tangent Bug
robot moves towards

## Slide 38: Tangent Bug
robot after moving

## Slide 39: Tangent Bug
  update , ,

## Slide 40: Tangent Bug
robot moves towards

## Slide 41: Tangent Bug
update , ,

## Slide 42: Tangent Bug
sometime later on (still in "boundary following" mode)

## Slide 43: Tangent Bug
  update , ,

## Slide 44: Tangent Bug
sometime later on (still in "boundary following" mode)

## Slide 45: Tangent Bug
  update , ,

## Slide 46: Tangent Bug
sometime later on (still in "boundary following" mode)

## Slide 47: Tangent Bug
  update , ,

## Slide 48: Tangent Bug
eventually the robot reaches a point where
when this occurs the robot resumes "motion to goal" mode

## Slide 49: Tangent Bug
behavior when range sensor has a maximum distance of 0

## Slide 50: Tangent Bug
behavior when range sensor has a maximum distance of

## Slide 51: Tangent Bug
behavior when range sensor has a maximum distance of

## Slide 52: Tangent Bug
behavior when range sensor has a maximum distance of

## Slide 53: Tangent Bug
behavior when range sensor has a finite maximum distance

## Slide 54: Tangent Bug
full details
  Principles of Robot Motion: Theory, Algorithms, and Implementations
  http://www.library.yorku.ca/find/Record/2154237
nice animation
  http://www.cs.cmu.edu/~motionplanning/student_gallery/2006/st/hw2pub.htm