## Slide 1: Distance Sensor Models

## Slide 2: Range Sensors
range sensors measure the distance between the robot and the sensed object(s)
  bearing measurement can be obtained by rotating the sensor or using multiple sensors arranged on a circular arc
many non-vision based sensors can be modeled by measuring the distance along a beam or cone

## Slide 3: Infra-red Range Sensor
uses an IR LED and a linear CCD array to triangulate distances
object
object
angle increases as distance increases
Sharp GP2Y0A21YK0F data sheet

## Slide 4: Infra-red Range Sensor
has a minimum and maximum distance
  changes depending on the model but range is on the order of a few centimeters to a few meters
inexpensive (less than $20)
measurements affected by the material properties of the object
  but less sensitive to the orientation of the reflecting surface
low accuracy

## Slide 5: Ultrasound Range Sensors
ultrasound is sound above the upper limit of human hearing (approximately 20,000 Hz)
inexpensive ultrasonic transducers are essentially ceramic discs that vibrate at ultrasonic frequencies
  operate via the piezoelectric effect
    an applied external electric field causes a small change in the physical dimensions
    conversely, an applied stress will induce a small electric field

## Slide 6: Ultrasound Range Sensors
basic idea of operation is simple
  transducer emits a short pulse of ultrasound
  receiver listens for echo
  time elapsed between pulse and echo is proportional to twice the distance to the object

## Slide 7: Ultrasound Range Sensors
speed of sound in air is given approximately by where T is temperature in Celsius
  humidity affects c
modern electronics can easily measure elapsed time with sufficient precision to obtain good distance resolution

## Slide 8: Ultrasound Range Sensors
most materials are specular reflectors of ultrasound

## Slide 9: Ultrasound Range Sensors
multiple reflections produce erroneous distance measurements
Strickland and King, “Characteristics of Ultrasonic Ranging Sensors in an Underground Environment”

## Slide 10: Ultrasound Range Sensors
unfocussed ultrasound transducers have a wide beam pattern with significant side lobes
Cao and Borenstein, “Experimental Characterization of Polaroid Ultrasonic Sensors in Single and Phased Array Configuration”

## Slide 11: Ultrasound Range Sensors
beamwidth + side lobes leads to spurious measurements
Cao and Borenstein, “Experimental Characterization of Polaroid Ultrasonic Sensors in Single and Phased Array Configuration”

## Slide 12: Time of Flight Sensor
https://www.adafruit.com/product/3317
appear in laser tape measures
array of time of flight sensors are use in time of flight cameras

## Slide 13: LIDAR
light detection and ranging
commercial range finder disassembled

## Slide 14: LIDAR
for time of flight sensor
  speed of light 1 ns = 150 mm 100 ps = 15 mm 10 ps = 1.5 mm
typical angular resolution below 1 degree
typical errors on the order of 10 cm or less
cost > $1,000

## Slide 15: Beam Models of Range Finders
given the map and the robot’s location, find the probability density that the range finder detects an object at a distance along a beam
the k is here because range sensors typically return many measurements at one time; e.g., the sensor might return a full 360 degree scan made up of K measurements at once

## Slide 16: Beam Models of Range Finders
most range finders have a minimum and maximum range
we seek a model that can represent
  the correct range measurement with noise
  unexpected obstacles
  failures
  random measurements
1
2
3

## Slide 17: Beam Models of Range Finders
Correct Measurement with Noise
suppose that the beam intersects an obstacle at a range of
  model this measurement as a narrow Gaussian with mean

## Slide 18: Beam Models of Range Finders
Unexpected Obstacles
in a dynamic environment there will be obstacles not found on a static map; these obstacles will cause range measurements shorter than expected
if such obstacles appear continuously and independently at a constant average rate then they can be modeled as a Poisson process
the time between events in a Poisson process has an exponential distribution with probability density function

## Slide 19: Beam Models of Range Finders

## Slide 20: Beam Models of Range Finders
Failures
range finders can fail to sense an obstacle in which case most sensors return
modeled as a point mass distribution centered at

## Slide 21: Beam Models of Range Finders
Random Measurements
unexplainable measurements are modeled as a uniform distribution over the range [0, ]

## Slide 22: Beam Models of Range Finders
the complete model is a weighted sum of the previous four densities with weights