## Slide 1: CSE4421/5324: Introduction to Robotics

## Slide 2: Contact Information
Burton Ma Lassonde 2046 burton@cse.yorku.ca
EECS4421/5324 lectures Monday, Wednesday, Friday 1:30-2:30PM (SLH C) Lab 1 Thursday 12:30-2:30, Prism 1004 Lab 2 Thursday 2:30-4:30, Prism 1004
www.eecs.yorku.ca/course/4421 (web site not complete yet)

## Slide 3: General Course Information
introduces the basic concepts of robotic manipulators and autonomous systems. After a review of some fundamental mathematics the course examines the mechanics and dynamics of robot arms, mobile robots, their sensors and algorithms for controlling them.

## Slide 4: Textbook
no required textbook
first 6 weeks of course uses notation consistent with Robot Modeling and Control by MW Spong, S Hutchinson, M Vidyasagar

## Slide 5: Assessment
labs/assignments 6 x 5%
midterm, 30%
exam, 40%

## Slide 6: Introduction to manipulator kinematics

## Slide 7: Robotic Manipulators
a robotic manipulator is a kinematic chain
  i.e. an assembly of pairs of rigid bodies that can move respect to one another via a mechanical constraint
the rigid bodies are called links
the mechanical constraints are called joints

## Slide 8: A150 Robotic Arm
link 3
link 2

## Slide 9: Joints
most manipulator joints are one of two types
revolute (or rotary)
  like a hinge
prismatic (or linear)
  like a piston
our convention: joint i connects link i – 1 to link i
  when joint i is actuated, link i moves

## Slide 10: Joint Variables
revolute and prismatic joints are one degree of freedom (DOF) joints; thus, they can be described using a single numeric value called a joint variable
qi : joint variable for joint i
revolute
  qi = qi : angle of rotation of link i relative to link i – 1
prismatic
  qi = di : displacement of link i relative to link i – 1

## Slide 11: Revolute Joint Variable
revolute
  like a hinge
  allows relative rotation about a fixed axis between two links
    axis of rotation is the z axis by convention
joint variable qi = qi : angle of rotation of link i relative to link i – 1
link i – 1
link i
qi
joint i

## Slide 12: Prismatic Joint Variable
prismatic
  like a piston
  allows relative translation along a fixed axis between two links
    axis of translation is the z axis by convention
  joint variable qi = di : displacement of link i relative to link i – 1
link i – 1
link i
di
joint i

## Slide 13: Common Manipulator Arrangments
most industrial manipulators have six or fewer joints
  the first three joints are the arm
  the remaining joints are the wrist
it is common to describe such manipulators using the joints of the arm
  R: revolute joint
  P: prismatic joint

## Slide 14: Articulated Manipulator
RRR (first three joints are all revolute)
joint axes
  z0 : waist
  z1 : shoulder (perpendicular to z0)
  z2 : elbow (parallel to z1)
z0
z1
z2
waist
shoulder
elbow
forearm
q1
q2
q3

## Slide 15: Spherical Manipulator
RRP
Stanford arm
  http://infolab.stanford.edu/pub/voy/museum/pictures/display/robots/IMG_2404ArmFrontPeekingOut.JPG
z0
z1
z2
waist
shoulder
q1
q2
d3

## Slide 16: SCARA Manipulator
RRP
Selective Compliant Articulated Robot for Assembly
  http://www.robots.epson.com/products/g-series.htm
z0
z1
z2
q1
q2
d3

## Slide 17: Parallel Robots
all of the preceding examples are examples of serial chains
  base (link 0) is connected to link 1 by a joint
  link 1 is connected to link 2 by a joint
  link 2 is connected to link 3 by a joint ... and so on
a parallel robot is formed by connecting two or more serial chains
  https://www.youtube.com/watch?v=p1Lrz0gPvOA

## Slide 18: Forward Kinematics
given the joint variables and dimensions of the links what is the position and orientation of the end effector?
q2
q1
a1
a2

## Slide 19: Forward Kinematics
choose the base coordinate frame of the robot
  we want (x, y) to be expressed in this frame
q2
q1
a1
a2
(x, y) ?
x0
y0

## Slide 20: Forward Kinematics
notice that link 1 moves in a circle centered on the base frame origin
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )

## Slide 21: Forward Kinematics
choose a coordinate frame with origin located on joint 2 with the same orientation as the base frame
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1

## Slide 22: Forward Kinematics
notice that link 2 moves in a circle centered on frame 1
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )

## Slide 23: Forward Kinematics
because the base frame and frame 1 have the same orientation, we can sum the coordinates to find the position of the end effector in the base frame
q2
q1
a1
a2
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )
(a1 cos q1 + a2 cos (q1 + q2),
a1 sin q1 + a2 sin (q1 + q2) )

## Slide 24: Forward Kinematics
we also want the orientation of frame 2 with respect to the base frame
  x2 and y2 expressed in terms of x0 and y0
q2
q1
a1
a2
x0
y0
q1
x2
y2

## Slide 25: Forward Kinematics
without proof I claim:
q2
q1
a1
a2
x0
y0
q1
x2 = (cos (q1 + q2),
sin (q1 + q2) )
y2 = (-sin (q1 + q2),
cos (q1 + q2) )
x2
y2

## Slide 26: Forward Kinematics
find , , and expressed in frame
d1
x0
y0
q2
x2
y2
x1
y1
(x, y) ?

## Slide 27: Forward Kinematics
find , , and expressed in frame
x0
y0
d1
q2
x2
y2
x1
y1
(x, y) ?

## Slide 28: Inverse Kinematics
given the position (and possibly the orientation) of the end effector, and the dimensions of the links, what are the joint variables?
q2 ?
q1 ?
a1
a2
x0
y0
x2
y2
(x, y)

## Slide 29: Inverse Kinematics
harder than forward kinematics because there is often more than one possible solution
a1
a2
x0
y0
(x, y)

## Slide 30: Inverse Kinematics
law of cosines
q2 ?
a1
a2
x0
y0
(x, y)
b

## Slide 31: Inverse Kinematics
and we have the trigonometric identity
therefore,
We could take the inverse cosine, but this gives only one of the two solutions.

## Slide 32: Inverse Kinematics
to obtain
Instead, use the two trigonometric identities:
which yields both solutions for q2 . In many programming languages you would use the
four quadrant inverse tangent function atan2
c2 = (x*x + y*y – a1*a1 – a2*a2) / (2*a1*a2);
s2 = sqrt(1 – c2*c2);
theta21 = atan2(s2, c2);
theta22 = atan2(-s2, c2);

## Slide 33: Inverse Kinematics
Exercise for the student: show that

## Slide 34: Spatial Descriptions

## Slide 35: Points and Vectors
point : a location in space
vector : magnitude (length) and direction between two points

## Slide 36: Coordinate Frames
choosing a frame (a point and two perpendicular vectors of unit length) allows us to assign coordinates

## Slide 37: Coordinate Frames
the coordinates change depending on the choice of frame

## Slide 38: Dot Product
the dot product of two vectors

## Slide 39: Vector Projection and Rejection
if u and v are unit vectors (have magnitude equal to 1) then the projection becomes
projection of u on v
rejection of u from v

## Slide 40: Translation
suppose we are given o1 expressed in {0}

## Slide 41: Translation 1
the location of {1} expressed in {0}

## Slide 42: Translation 1
the translation vector can be interpreted as the location of frame {j} expressed in frame {i}

## Slide 43: Translation 2
p1 expressed in {0}
a point expressed
in frame {1}

## Slide 44: Translation 2
the translation vector can be interpreted as a coordinate transformation of a point from frame {j} to frame {i}

## Slide 45: Translation 3
q0 expressed in {0}

## Slide 46: Translation 3
the translation vector can be interpreted as an operator that takes a point and moves it to a new point in the same frame

## Slide 47: Rotation
suppose that frame {1} is rotated relative to frame {0}

## Slide 48: Rotation 1
the orientation of frame {1} expressed in {0}

## Slide 49: Rotation 1
the rotation matrix can be interpreted as the orientation of frame {j} expressed in frame {i}

## Slide 50: Rotation 2
p1 expressed in {0}

## Slide 51: Rotation 2
the rotation matrix can be interpreted as a coordinate transformation of a point from frame {j} to frame {i}

## Slide 52: Rotation 3
q0 expressed in {0}

## Slide 53: Rotation 3
the rotation matrix can be interpreted as an operator that takes a point and moves it to a new point in the same frame

## Slide 54: Properties of Rotation Matrices
RT = R-1
the columns of R are mutually orthogonal
each column of R is a unit vector
det R = 1 (the determinant is equal to 1)

## Slide 55: Rotation and Translation

## Slide 56: Rotations in 3D

## Slide 57: Rotations

## Slide 58: Properties of Rotation Matrices
RT = R-1
the columns of R are mutually orthogonal
each column of R is a unit vector
det R = 1 (the determinant is equal to 1)

## Slide 59: Rotations in 3D

## Slide 60: Rotation About z-axis
+'ve rotation

## Slide 61: Rotation About x-axis
+'ve rotation

## Slide 62: Rotation About y-axis
+'ve rotation

## Slide 63: Relative Orientation Example

## Slide 64: Successive Rotations in Moving Frames
Suppose you perform a rotation in frame {0} to obtain {1}.
Then you perform a rotation in frame {1} to obtain {2}.
What is the orientation of {2} relative to {0}?

## Slide 65: Successive Rotations in a Fixed Frame
Suppose you perform a rotation in frame {0} to obtain {1}.
Then you rotate {1} in frame {0} to obtain {2}.
What is the orientation of {2} relative to {0}?

## Slide 66: Composition of Rotations
Given a fixed frame {0} and a current frame {1} and
  if {2} is obtained by a rotation R in the current frame {1} then use postmulitplication to obtain:
Given a fixed frame {0} and a frame {1} and
  if {2} is obtained by a rotation R in the fixed frame {0} then use premultiplication to obtain:

## Slide 67: Rotation About a Unit Axis

## Slide 68: Rigid Body Transformations

## Slide 69: Homogeneous Representation
translation represented by a vector d
  vector addition
rotation represented by a matrix R
  matrix-matrix and matrix-vector multiplication
convenient to have a uniform representation of translation and rotation
  obviously vector addition will not work for rotation
  can we use matrix multiplication to represent translation?

## Slide 70: Homogeneous Representation
consider moving a point p by a translation vector d
not possible as matrix-vector multiplication always leaves the origin unchanged

## Slide 71: Homogeneous Representation
consider an augmented vector ph and an augmented matrix D

## Slide 72: Homogeneous Representation
the augmented form of a rotation matrix R3x3

## Slide 73: Rigid Body Transformations in 3D
{0}
{1}
{2}

## Slide 74: Rigid Body Transformations in 3D
suppose {1} is a rotated and translated relative to {0}
what is the pose (the orientation and position) of {1} expressed in {0} ?
{0}
{1}

## Slide 75: Rigid Body Transformations in 3D
suppose we use the moving frame interpretation (postmultiply transformation matrices)
  translate in {0} to get {0’}
  and then rotate in {0’} to get {1}
{0}
{1}
{0}
{0’}
{0’}
Step 1
Step 2

## Slide 76: Rigid Body Transformations in 3D
suppose we use the fixed frame interpretation (premultiply transformation matrices)
  rotate in {0} to get {0’}
  and then translate in {0} in to get {1}
{0}
{0}
{0’}
{0’}
{1}
Step 1
Step 2

## Slide 77: Rigid Body Transformations in 3D
both interpretations yield the same transformation

## Slide 78: Homogeneous Representation
every rigid-body transformation can be represented as a rotation followed by a translation in the same frame
  as a 4x4 matrix
  where R is a 3x3 rotation matrix and d is a 3x1 translation vector

## Slide 79: Homogeneous Representation
in some frame i
  points
  vectors

## Slide 80: Inverse Transformation
the inverse of a transformation undoes the original transformation
  if
  then

## Slide 81: Transform Equations
{0}
{1}
{2}
{3}
{4}

## Slide 82: Transform Equations
give expressions for:

## Slide 83: Transform Equations
{0}
{1}
{2}
{3}

## Slide 84: Transform Equations
how can you find