## Slide 1: Unscented Kalman Filter

## Slide 2: Linearization via Unscented Transform
EKF
UKF

## Slide 3: Unscented Transform
intuition: it should be easier to approximate a given distribution than it is to approximate an arbitrary non-linear function
  it is easy to transform a point through a non-linear function
  use a set of points that capture the mean and covariance of the distribution, transform the points through the non-linear function, then compute the (weighted) mean and covariance of the transformed points

## Slide 4: Empirical transformation of a Gaussian random variable
% generate 500,000 samples from N(0, 1)
x = randn(1, 500000);
% draw the histogram of x
xc = -5:0.2:5;
nx = hist(x, xc);
bar(xc, nx, 1);
% transform each sample by f(x)
y = nthroot(x – 1, 3);
% draw the histogram of y
xc = -2:0.1:2;
ny = hist(y, xc);
bar(xc, ny, 1);

## Slide 5: Empirical transformation of a Gaussian random variable
-transform 500,000 random
samples through a non-linear
function

## Slide 6: Unscented Transform
-transform 3 carefully chosen
samples through a non-linear
function
-samples are called sigma points

## Slide 7: UKF Sigma-Point Estimate (2)
EKF
UKF

## Slide 8: UKF Sigma-Point Estimate (3)
EKF
UKF

## Slide 9: UKF Sigma-Point Estimate (4)

## Slide 10: Unscented Transform
for an n-dimensional Gaussian with mean μ and covariance Σ , the unscented transform uses 2n+1 sigma points (and associated weights)
Sigma points Weights

## Slide 11: Unscented Transform
choose κ ≥ 0 to guarantee a “reasonable” covariance matrix
  value is not critical, so choose κ = 0 by default
choose 0 ≤ α ≤ 1
  controls the spread of the sigma point distribution; should be small when nonlinearities are strong
choose β ≥ 0
  β = 2 is optimal if distribution is Gaussian

## Slide 12: Unscented Transform
Pass sigma points through nonlinear function
Recover mean and covariance

## Slide 13
UKF_localization ( mt-1, St-1, ut, zt, m):
Prediction:
Control noise
Measurement noise
Augmented state mean
Augmented covariance
Sigma points
Prediction of sigma points
Predicted mean
Predicted covariance

## Slide 14
UKF_localization ( mt-1, St-1, ut, zt, m):
Correction:
Measurement sigma points
Predicted measurement mean
Pred. measurement covariance
Cross-covariance
Kalman gain
Updated mean
Updated covariance

## Slide 15: Augmented state
to account for the control noise sigma points are generated for the control variables
to account for the measurement noise sigma points are generated for the measurement variables
all sigma points can be generated in a single step by using an augmented state vector

## Slide 16: Augmented state
Augmented state vector

## Slide 17: Augmented state sigma points
Generating sigma points with the augmented state yields sigma points each having components in state, control, and measurement

## Slide 18: Augmented state sigma points

## Slide 19: UKF Prediction Step

## Slide 20: UKF Observation Prediction Step

## Slide 21: UKF Correction Step

## Slide 22: Estimation Sequence
EKF PF UKF

## Slide 23: Estimation Sequence
EKF UKF

## Slide 24: Prediction Quality
EKF UKF
velocity_motion_model

## Slide 25: UKF Summary
Highly efficient: Same complexity as EKF, with a constant factor slower in typical practical applications
Better linearization than EKF: Accurate in first two terms of Taylor expansion (EKF only first term)
Derivative-free: No Jacobians needed
Still not optimal!